3GPP TSG-CT WG1 Meeting #127-e	C1-207166

# Electronic meeting; 13-20 November 2020

Source:	Qualcomm Incorporated

Title:	Solution <X> to Key Issue 2

Spec:	3GPP TR 24.821

Agenda item:	17.2.4

Document for:	Agreement

1. Introduction

In TR 24.821, Key Issue 2, CT1 agreed to address the following issues:

1)	how the UE determines which PLMN(s) can be selected in determined country of its physical location (if it is determined that the UE is not in an international area);

2)	what information could be available to the UE to help in selecting, in a given country, a PLMN that meets the LI requirements of that country:

a)	pre-configured in the UE; and

b)	provided by PLMN;

3)	what modifications are needed, if any, to the PLMN selelction procedure to take the LI requirement into account.

In this contribution, a solution to the issue 1) using option 2)a) is proposed. This solution is complimentary to the solution in C1-207167, which uses option 2)b).

2. Reason for Change

This solution tackles issue 1) using option 2)a). Specifically, for each PLMN listed in PLMN Selector files in USIM, there is an indication of the countries in which the PLMN can be selected.

3. Proposal

It is proposed to agree the following changes to 3GPP TR 24.821 v0.1.0.

* * * First Change * * * *

## 6.x	Solution <x>: Determining PLMNs that can be selected in the country of UE location based on USIM configuration

This is a candidate solution to Key Issue 2. It is relevant to the deployment scenario A and B (B1 through B3).

It is assumed that the UE knows in which country it is located. How this is achieved is a topic in Key Issue 1.

For each PLMN in the "HPLMN selector with Access Technology" and "User Controlled PLMN Selector with Access Technology" and "Operator Controlled PLMN Selector with Access Technology" files, there can be configured a list of countries in which the PLMN can be selected. This list is optional for each PLMN. If the list is not configured for a PLMN, the PLMN is considered as selectable only in the country of its MCC, unless the PLMN has a shared PLMN ID (MCC 9xx), in which case the PLMN is considered as selectable in all countries.

NOTE:	How the list of countries in which the PLMN can be selected is encoded in USIM is left to CT6 to discuss. The encoding should suppport all the relevant deployment scenarios.