3GPP TSG-CT WG1 Meeting #127-e	C1-207167

# Electronic meeting; 13-20 November 2020

Source:	Qualcomm Incorporated

Title:	Solution <y> to Key Issue 2

Spec:	3GPP TR 24.821

Agenda item:	17.2.4

Document for:	Agreement

1. Introduction

In TR 24.821, Key Issue 2, CT1 agreed to address the following issues:

1)	how the UE determines which PLMN(s) can be selected in determined country of its physical location (if it is determined that the UE is not in an international area);

2)	what information could be available to the UE to help in selecting, in a given country, a PLMN that meets the LI requirements of that country:

a)	pre-configured in the UE; and

b)	provided by PLMN;

3)	what modifications are needed, if any, to the PLMN selelction procedure to take the LI requirement into account.

In this contribution, a solution to the issue 1) using option 2)b) is proposed. This solution is complimentary to the solution in C1-207166, which uses option 2)a).

2. Reason for Change

This solution tackles issue 1) using option 2)b). Specifically, a PLMN broadacsts, in system information, the list of countries in which the PLMN can be selected.

3. Proposal

It is proposed to agree the following changes to 3GPP TR 24.821 v0.1.0.

* * * First Change * * * *

## 6.y	Solution <y>: Determining PLMNs that can be selected in the country of UE location based on system information

### 6.y.1	Target key issue

This is a candidate solution to Key Issue 2. It is relevant to the deployment scenario A and B (B1 through B3).

## 6.y.2	Solution description

It is assumed that the UE knows in which country it is located. How this is achieved is a topic in Key Issue 1.

In the system information, a PLMN can provide a list of countries in which the PLMN can be selected. This list is optional for each PLMN. If the list is not provided by a PLMN, the PLMN is considered as selectable only in the country of its MCC, unless the PLMN has a shared PLMN ID (MCC 9xx), in which case the PLMN is considered as selectable in all countries.

Editor’s Note:	This solution is dependent on the RAN agreement to broadcast a list of countries in which the PLMN can be selected in the system information.

Editor’s Note:	How the list of countries in which the PLMN can be selected is encoded (e.g. list of MCCs) is FFS.

## 6.y.3	Impacts

UE impacts:

-	New logic to eliminate candidate PLMNs based on the indication provided by each PLMN in the system information of the countries that the PLMN can be selected in.

Network impact:

-	Each PLMN optionally broadcasts in the system information a list of countries in which the PLMN can be selected.