3GPP TSG-CT WG1 Meeting #127-e	C1-20arg2

Electronic meeting, 13-20 November 2020	(revision of C1-207504, C1-207156, C1-206206)

| CR-Form-v12.0 |
| --- |
| CHANGE REQUEST |
|  | 23.122 | CR | 0600 | rev | 3 | Current version: | 17.0.0 |  |
| For HELP on using this form: comprehensive instructions can be found at http://www.3gpp.org/Change-Requests. |

| Proposed change affects: | UICC apps |  | ME | x | Radio Access Network |  | Core Network |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

| Title: | Handling of Higher Priority PLMN selection with the presence of “PLMNs where registration was aborted due to SOR” list |
| --- | --- |
| Source to WG: | Apple |
| Source to TSG: | C1 |
| Work item code: | 5GProtoc17 |  | Date: | 2020-11-16 |
| Category: | F |  | Release: | Rel-17 |
|  | Use one of the following categories: F (correction) A (mirror corresponding to a change in an earlier release) B (addition of feature), C (functional modification of feature) D (editorial modification) Detailed explanations of the above categories can be found in 3GPP TR 21.900. | Use one of the following releases: Rel-8 (Release 8) Rel-9 (Release 9) Rel-10 (Release 10) Rel-11 (Release 11) Rel-12 (Release 12) Rel-13 (Release 13) Rel-14 (Release 14) Rel-15 (Release 15) Rel-16 (Release 16) Rel-17 (Release 17) |
| Reason for change: | Currently UE maintains the list consisting of “PLMNs where registration was aborted due to SOR list” that was created when certain error conditions are met while handling SoR transparent container in Registration accept or DL NAS transport message. UE behavior is undefined when the list is present, and UE performs higher priority PLMN selection. Scenario 1: 1) UE already has list of “PLMNs where registration was aborted due to SOR”. 2) When UE has registered on VPLMN, it periodically looks for higher priority PLMN and attempt to obtain service on a higher priority PLMN as specified in subclause 4.4.3. 3) With the existing procedure defined, UE might end in the same VPLMN which is in the list of “PLMNs where registration was aborted due to SOR”, while it could have selected other PLMN from OPLMN. Scenario 2: 1) UE already has list of “PLMNs where registration was aborted due to SOR”. 2) When UE registers on a new high priority VPLMN and received equivalent PLMNs. 3) If received equivalent PLMNs are part of list of “PLMNs where registration was aborted due to SOR”, there is no existing procedure defined to prioritise amongst equivalent PLMNs, hence UE might select back an equivalent PLMN which is already in list of “PLMNs where registration was aborted due to SOR”. |
| Summary of change: | Add an exception clause for equivalent PLMNs in subclause "4.4.3.3.1 Automatic and manual network selection modes”. Add an new bullet i) which defines that in step iii) of subclause 4.4.3.1.1 the MS shall limit its attempts to access higher priority PLMN/access technology combinations to PLMN/access technology combinations which are not in the list of "PLMNs where registration was aborted due to SOR". If in step iii) of subclause 4.4.3.1.1 all entries of the "Operator Controlled PLMN Selector with Access Technology" of the same country as the current serving VPLMN are excluded as they are contained in the list of "PLMNs where registration was aborted due to SOR" (i.e. with step iii of subclause 4.4.3.1.1) no candidate is identified), the UE shall select and attempt registration, by scanning in accordance with the requirements that are applicable steps iv) and v) as defined in the Automatic Network Selection Mode in subclause 4.4.3.1.1. |
| Consequences if not approved: | UE might select back one of the VPLMN which is in the list of “PLMNs where registration was aborted due to SOR” and remain in that VPLMN and not select other high priority VPLMNs which might have fetched SOR from HPLMN. |
| Clauses affected: | 4.4.3.3.1 |
|  | Y | N |  |  |
| Other specs |  | X | Other core specifications | TS/TR ... CR ... |
| affected: |  | X | Test specifications | TS/TR ... CR ... |
| (show related CRs) |  | X | O&M Specifications | TS/TR ... CR ... |
| Other comments: |  |
| This CR's revision history: |  |

***** First change *****

#### 4.4.3.3	In VPLMN

##### 4.4.3.3.1	Automatic and manual network selection modes

If the MS is in a VPLMN, the MS shall periodically attempt to obtain service on its HPLMN (if the EHPLMN list is not present or is empty) or one of its EHPLMNs (if the EHPLMN list is present) or a higher priority PLMN/access technology combinations listed in "user controlled PLMN selector" or "operator controlled PLMN selector" by scanning in accordance with the requirements that are applicable to i), ii) and iii) as defined in the Automatic Network Selection Mode in subclause 4.4.3.1.1. In the case that the mobile has a stored "Equivalent PLMNs" list the mobile shall only select a PLMN if it is of a higher priority than those of the same country as the current serving PLMN which are stored in the "Equivalent PLMNs" list. For this purpose, a value of timer T may be stored in the SIM. The interpretation of the stored value depends on the radio capabilities supported by the MS:

-	For an MS that does not support any of the following: EC-GSM-IoT, Category M1 or Category NB1 (as defined in 3GPP TS 36.306 [54]), T is either in the range 6 minutes to 8 hours in 6 minute steps or it indicates that no periodic attempts shall be made. If no value for T is stored in the SIM, a default value of 60 minutes is used for T.

-	For an MS that only supports any of the following or a combination of: EC-GSM-IoT, Category M1 or Category NB1 (as defined in 3GPP TS 36.306 [54]), T is either in the range 2 hours to 240 hours, using 2 hour steps from 2 hours to 80 hours and 4 hour steps from 84 hours to 240 hours, or it indicates that no periodic attempts shall be made. If no value for T is stored in the SIM, a default value of 72 hours is used.

-	For an MS that supports both:

a)	any of the following or a combination of: EC-GSM-IoT, Category M1 or Category NB1 (as defined in 3GPP TS 36.306 [54]); and

b)	any access technology other than the following: EC-GSM-IoT, Category M1 or Category NB1 (as defined in 3GPP TS 36.306 [54]),

then T is interpreted depending on the access technology in use as specified below:

1)	if the MS is using any of the following at the time of starting timer T: EC-GSM-IoT, Category M1 or Category NB1 (as defined in 3GPP TS 36.306 [54]), T is either in the range 2 hours to 240 hours, using 2 hour steps from 2 hours to 80 hours and 4 hour steps from 84 hours to 240 hours, or it indicates that no periodic attempts shall be made. If no value for T is stored in the SIM, a default value of 72 hours is used; and

2)	if the MS is not using any of the following at the time of starting timer T: EC-GSM-IoT, Category M1 or Category NB1 (as defined in 3GPP TS 36.306 [54]), T is either in the range 6 minutes to 8 hours in 6 minute steps or it indicates that no periodic attempts shall be made. If no value for T is stored in the SIM, a default value of 60 minutes is used for T.

If the MS is configured with the MinimumPeriodicSearchTimer as specified in 3GPP TS 24.368 [50] or 3GPP TS 31.102 [40], the MS shall not use a value for T that is less than the MinimumPeriodicSearchTimer. If the value stored in the SIM, or the default value for T (when no value is stored in the SIM), is less than the MinimumPeriodicSearchTimer, then T shall be set to the MinimumPeriodicSearchTimer.

The MS does not stop timer T, as described in 3GPP TS 24.008 [23] and 3GPP TS 24.301 [23A], when it activates power saving mode (PSM) (see 3GPP TS 23.682 [27A]).

The MS can be configured for Fast First Higher Priority PLMN search as specified in 3GPP TS 31.102 [40] or 3GPP TS 24.368 [50]. Fast First Higher Priority PLMN search is enabled if the corresponding configuration parameter is present and set to enabled. Otherwise, Fast First Higher Priority PLMN search is disabled.

The attempts to access the HPLMN or an EHPLMN or higher priority PLMN shall be as specified below:

a)	The periodic attempts shall only be performed in automatic mode when the MS is roaming, and not while the MS is attached for emergency bearer services, is registered for emergency services, has a PDU session for emergency services or has a PDN connection for emergency bearer services;

b)	The MS shall make the first attempt after a period of at least 2 minutes and at most T minutes:

-	only after switch on if Fast First Higher Priority PLMN search is disabled; or

-	after switch on or upon selecting a VPLMN if Fast First Higher Priority PLMN search is enabled.

c)	The MS shall make the following attempts if the MS is on the VPLMN at time T after the last attempt;

d)	Periodic attempts shall only be performed by the MS while in idle mode;

d1)	Periodic attempts may be postponed while the MS is in power saving mode (PSM) (see 3GPP TS 23.682 [27A]).

d2)	Periodic attempts may be postponed while the MS is receiving eMBMS transport service in idle mode (see 3GPP TS 23.246 [68]).

d3)	Periodic attempts may be postponed till the next eDRX occasion while the MS is configured with eDRX.

d4)	Periodic attempts may be postponed while the MS is in relaxed monitoring (see 3GPP TS 36.304 [43]).

e)	If the HPLMN (if the EHPLMN list is not present or is empty) or a EHPLMN (if the list is present) or a higher priority PLMN is not found, the MS shall remain on the VPLMN.

f)	In steps i), ii) and iii) of subclause 4.4.3.1.1 the MS shall limit its attempts to access higher priority PLMN/access technology combinations to PLMN/access technology combinations of the same country as the current serving VPLMN, as defined in Annex B.

g)	Only the priority levels of Equivalent PLMNs of the same country as the current serving VPLMN, as defined in Annex B, and which are not in the list of "PLMNs where registration was aborted due to SOR" shall be taken into account to compare with the priority level of a selected PLMN.

h)	If the PLMN of the highest priority PLMN/access technology combination available is the current VPLMN, or one of the PLMNs in the "Equivalent PLMNs" list, the MS shall remain on the current PLMN/access technology combination.

i)	In step iii) of subclause 4.4.3.1.1 the MS shall limit its attempts to access higher priority PLMN/access technology combinations to PLMN/access technology combinations which are not in the list of "PLMNs where registration was aborted due to SOR".

If in step iii) of subclause 4.4.3.1.1 all entries of the "Operator Controlled PLMN Selector with Access Technology" of the same country as the current serving VPLMN are excluded as they are contained in the list of "PLMNs where registration was aborted due to SOR" (i.e. with step iii) of subclause 4.4.3.1.1 no candidate is identified), the UE shall select and attempt registration, by scanning in accordance with the requirements that are applicable to steps iv) and v) as defined in the Automatic Network Selection Mode in subclause 4.4.3.1.1.

***** End of changes *****