3GPP TSG-CT WG1 Meeting #127-e	C1-20XXXX was7107

Electronic meeting, 13-20 November 2020

| CR-Form-v12.0 |
| --- |
| CHANGE REQUEST |
|  | 23.122 | CR | 0625 | rev | 1 | Current version: | 17.0.0 |  |
| For HELP on using this form: comprehensive instructions can be found at http://www.3gpp.org/Change-Requests. |

| Proposed change affects: | UICC apps | X | ME | x | Radio Access Network |  | Core Network |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

| Title: | Initial CAG information list |
| --- | --- |
| Source to WG: | MediaTek |
| Source to TSG: | C1 |
| Work item code: | 5GProtoc17 |  | Date: | 2020-11-17 |
| Category: | B |  | Release: | Rel-17 |
|  | Use one of the following categories: F (correction) A (mirror corresponding to a change in an earlier release) B (addition of feature), C (functional modification of feature) D (editorial modification) Detailed explanations of the above categories can be found in 3GPP TR 21.900. | Use one of the following releases: Rel-8 (Release 8) Rel-9 (Release 9) Rel-10 (Release 10) Rel-11 (Release 11) Rel-12 (Release 12) Rel-13 (Release 13) Rel-14 (Release 14) Rel-15 (Release 15) Rel-16 (Release 16) |
| Reason for change: | At CT1#125-e, the use case of a device not configured with any CAG information list, which needs to register to a CAG cell in automatic network selection mode to be provisioned, was discussed. One way to address this use case is to enable storage of a pre-configured CAG information list in the USIM. |
| Summary of change: | When a USIM is inserted, if the UE has a "CAG information list" stored in the USIM, the UE copies the "CAG information list" from the USIM to the ME. Additionally, the Allowed CAG range is indicated in the CAG information list stored in the USIM and the ME. |
| Consequences if not approved: | A device not configured with any CAG information list in automatic network selection mode cannot receive a CAG information list from a CAG cell. |
| Clauses affected: | 3.8 |
|  | Y | N |  |  |
| Other specs |  | X | Other core specifications | TS/TR ... CR ... |
| affected: |  | X | Test specifications | TS/TR ... CR ... |
| (show related CRs) |  | X | O&M Specifications | TS/TR ... CR ... |
| Other comments: |  |
| This CR's revision history: |  |

***** change *****

## 3.8	CAG selection (N1 mode only)

The MS may support CAG.

If the MS supports CAG, the MS can be provisioned by the network with a "CAG information list", consisting of zero or more entries, each containing:

a)	a PLMN ID;

b)	an "Allowed CAG list". The "Allowed CAG list" contains either zero or more CAG-IDs or "Allowed CAG range" consists of the lowest allowed CAG-ID and the highest allowed CAG-ID; and

NOTE X:	The "Allowed CAG range" can be part of the "CAG information list" stored in the ME or stored in the USIM. The "Allowed CAG range" is not part of the "CAG information list" sent in NAS signalling.

c)	an optional "indication that the MS is only allowed to access 5GS via CAG cells".

The "CAG information list" provisioned by the network is stored in the ME.

NOTE 1:	When the MS is registering or registered to a PLMN other than the HPLMN, a PLMN equivalent to the HPLMN or EHPLMN, then the HPLMN will send a "CAG information list" consisting of CAG subscription information related to the serving PLMN only. When the MS is registering or registered to the HPLMN, a PLMN equivalent to the HPLMN or EHPLMN then the HPLMN or EHPLMN may send CAG subscription information related to any PLMN in the "CAG information list".

In addition, the MS can also be pre-configured with a "CAG information list" stored in the USIM (see 3GPP TS 31.102 [40]).

Editor's note (WI 5GProtoc17, CR#0611):	"CAG information list" stored in the USIM is to be specified by CT6.

When a USIM is inserted, if:

-	no "CAG information list" is stored in the non-volatile memory of the ME as specified in 3GPP TS 24.501 [64] annex C; or

-	the SUPI from the USIM does not match the SUPI stored together with the "CAG information list" in the non-volatile memory of the ME as specified in 3GPP TS 24.501 [64] annex C;

and the MS has a "CAG information list" stored in the USIM (see 3GPP TS 31.102 [22]), the MS shall delete the "CAG information list" stored in the ME, if any, and store the "CAG information list" from the USIM in the ME as specified in 3GPP TS 24.501 [64] annex C.

NOTE 2:	The MS ignores the "CAG information list" stored in the USIM except when the USIM is inserted.

If the MS supports CAG and a PLMN is selected as described in subclause 4.4.3.1.1, the automatic CAG selection is performed as part of subclause 4.4.3.1.1.

If the MS supports CAG and a PLMN is selected as described in subclause 4.4.3.1.2, the manual CAG selection is performed as part of subclause 4.4.3.1.2.

The NAS shall provide the AS with a "CAG information list", if available. If the contents of the "CAG information list" have changed, the NAS shall provide an updated "CAG information list" to the AS.