3GPP TSG-CT WG1 Meeting #127-e	C1-20XXXX

Electronic meeting, 13-20 November 2020

| CR-Form-v12.0 |
| --- |
| CHANGE REQUEST |
|  | 23.122 | CR | 0625 | rev | - | Current version: | 17.0.0 |  |
| For HELP on using this form: comprehensive instructions can be found at http://www.3gpp.org/Change-Requests. |

| Proposed change affects: | UICC apps | X | ME | x | Radio Access Network |  | Core Network |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

| Title: | [Solution Option 2.4] Initial CAG information list stored in the USIM and Allowed CAG Range in CAG information list |
| --- | --- |
| Source to WG: | Mediatek Inc., China Mobile?, Ericsson? |
| Source to TSG: | C1 |
| Work item code: | 5GProtoc17 |  | Date: | 2020-11-16 |
| Category: | B |  | Release: | Rel-17 |
|  | Use one of the following categories: F (correction) A (mirror corresponding to a change in an earlier release) B (addition of feature), C (functional modification of feature) D (editorial modification) Detailed explanations of the above categories can be found in 3GPP TR 21.900. | Use one of the following releases: Rel-8 (Release 8) Rel-9 (Release 9) Rel-10 (Release 10) Rel-11 (Release 11) Rel-12 (Release 12) Rel-13 (Release 13) Rel-14 (Release 14) Rel-15 (Release 15) Rel-16 (Release 16) |
| Reason for change: | As discussed in CT1-124e, there is a deployment demand to enable a UE supporting CAG but without "CAG information list" to access a CAG-only "NG-RAN" in the automatic network selection mode A solution in C1-207069 (Initial CAG information list stored in USIM) is proposed, however it is difficult to use this solution because it is difficult for operators to predict and pre-configure different number of CAG-IDs into different number of USIMs based on different customers' requirements in advance. To further satisfy operators practical deployment requirements, based on the solution specified in e.g., C1-207069, Additionally a new "Allowed CAG Range" is introduced: - The "Allowed CAG Range" is specified by "minimum Allowed CAG ID and maximum Allowed CAG ID", which means the CAG IDs between minimum ~ maximum are allowed. - A lot of similar concepts can be seen in SPEC, e.g., - In TAI list, type of list = "01" of "5GS tracking area identity list" as specified in 24.501 9.11.3.9 which indicate the beginning TAC and a 5 bits "Number of elements" to indicate a range of TACs in a single IE, e.g., : - Beginning TAC 0x111111 and "Number of elements" == 32, means that the TACs beginning from 0x111111 ~ 0x111111 + 32 -1 are assigned TACs - In Match-all type, IPv6 remote address/prefix length type, IPv6 local address/prefix length type, Local port range type, Remote port range type, as specified in 24.501 9.11.4.13 |
| Summary of change: | 1. The "CAG information list" can be stored in USIM (same as C1-207069) 2. When a USIM is inserted, if the UE has a "CAG information list" stored in the USIM, the UE copies the "CAG information list" from the USIM to the ME. (same as C1-207069) 3. New "Allowed CAG Range" is added into the entry of "CAG information list", allowing the operator to configure a range of allowed CAG IDs. |
| Consequences if not approved: | Lack of flexible allowed CAG ID assignment method blocking the PNI-NPN bussiness planning of operators. |
| Clauses affected: | 3.8 |
|  | Y | N |  |  |
| Other specs |  | X | Other core specifications | TS/TR ... CR ... |
| affected: |  | X | Test specifications | TS/TR ... CR ... |
| (show related CRs) |  | X | O&M Specifications | TS/TR ... CR ... |
| Other comments: |  |
| This CR's revision history: |  |

***** change *****

## 3.8	CAG selection (N1 mode only)

The MS may support CAG.

If the MS supports CAG, the MS can be provisioned by the network with a "CAG information list". In addition, the MS can be pre-configured with a "CAG information list" stored in the USIM (see 3GPP TS 31.102 [40]).

Editor's note (WI 5GProtoc17, CR#0625):	"CAG information list" stored in the USIM is to be specified by CT6.

The "CAG information list" consists of zero or more entries, each containing:

a)	a PLMN ID;

b)	an "Allowed CAG list". The "Allowed CAG list" contains

1)	zero or more CAG-IDs; or

2)	a "Allowed-CAG-Range"; and

c)	an optional "indication that the MS is only allowed to access 5GS via CAG cells".

NOTE X:	In this release of specification, the "Allowed-CAG-Range" is only applicable for "CAG information list" stored in USIM.

The "CAG information list" provisioned by the network is stored in the ME.

NOTEX:	When the MS is registering or registered to a PLMN other than the HPLMN, a PLMN equivalent to the HPLMN or EHPLMN, then the HPLMN will send a "CAG information list" consisting of CAG subscription information related to the serving PLMN only. When the MS is registering or registered to the HPLMN, a PLMN equivalent to the HPLMN or EHPLMN then the HPLMN or EHPLMN may send CAG subscription information related to any PLMN in the "CAG information list". When a USIM is inserted, if:

-	no "CAG information list" is stored in the non-volatile memory of the ME as specified in 3GPP TS 24.501 [64] annex C; or

-	the SUPI from the USIM does not match the SUPI stored together with the "CAG information list" in the non-volatile memory of the ME as specified in 3GPP TS 24.501 [64] annex C;

and the MS has a "CAG information list" stored in the USIM (see 3GPP TS 31.102 [22]), the MS shall delete the "CAG information list" stored in the ME, if any, and store the "CAG information list" from the USIM in the ME as specified in 3GPP TS 24.501 [64] annex C.

NOTE X:	The MS ignores the "CAG information list" stored in the USIM except when the USIM is inserted.

If the MS supports CAG and a PLMN is selected as described in subclause 4.4.3.1.1, the automatic CAG selection is performed as part of subclause 4.4.3.1.1.

If the MS supports CAG and a PLMN is selected as described in subclause 4.4.3.1.2, the manual CAG selection is performed as part of subclause 4.4.3.1.2.

The NAS shall provide the AS with a "CAG information list", if available. If the contents of the "CAG information list" have changed, the NAS shall provide an updated "CAG information list" to the AS.

***** end of change *****