3GPP TSG-CT WG1 Meeting #127-e	C1-20xxxx

# Electronic meeting; 13-20 November 2020

Source:	Nokia, Nokia Shanghai Bell

Title:	Solution for key issue 1

Spec:	3GPP TR 24.821 V0.1.0

Agenda item:	17.2.4

Document for:	Agreement

1. Introduction

<Introduction part (optional)>

2. Reason for Change

A solution for key issue 1 is proposed for the progress of the work.

3. Conclusions

<Conclusion part (optional)>

4. Proposal

It is proposed to agree the following changes to 3GPP TR 24.821 V0.1.0.

* * * First Change * * * *

## 6.x	Solution X

### 6.x.1	Target key issue

This solution addresses key issue #1.

### 6.x.1	Solution description

The salient features of the solution are as follows.

a)	How the UE determines the country of its physical location and whether it is in the scope of 3GPP

The solution relies on various locating methods, which are specific to UE implementation. Therefore, even for legacy UEs, no hardware change is required.

Editor's note:	It is FFS whether a UE incapable of locating itself should be considered.

The mapping (physical location to a country/international area) information provisioned in the UE is used to determine the country/internation area of its physical location. How to provision this information to the UE is outside the scope of 3GPP in this solution.

b)	To what extent and under which conditions the UE could still rely on the MCC of the serving PLMN to determine the country of its physical location

It is assumed that a UE which could not select:

-	a PLMN whose MCC does not correspond to the country of its physical location; or

-	a PLMN whose MCC is included in the list of MCCs recommended by the network (where the list of recommended MCCs is provided via NAS signaling);

is in a "particular" state and a PLMN ensures that a UE not in the "particular" state is served by a PLMN whose MCC corresponds to the country of tis physical location. Therefore, a UE in the "particular" state which is served by a PLMN can rely on the MCC of the serving PLMN to determine the country of its physical location.

Editor's note:	It is FFS whether the "particular" state can be the limited service state or a new state.

Editor's note:	How the network can know that a UE is in the "particular" state is FFS.

### 6.x.3	Impacts to existing procedures due to the solution

UE:

-	A UE which could not select a PLMN whose MCC does not correspond to the country of its physical location or a PLMN whose MCC is included in the list of MCCs recommended by the network has to be in a "particular" state.

-	A UE in the "particular" state needs to be able to indicate to the network that the UE is in the "particular" state.

Network:

-	The network should be able to handle a UE in the "particular state".