3GPP TSG-CT WG1 Meeting #127-e	C1-20xxxx

# Electronic meeting; 13-20 November 2020

Source:	Nokia, Nokia Shanghai Bell

Title:	Solution for key issue 2

Spec:	3GPP TR 24.821 V0.1.0

Agenda item:	17.2.4

Document for:	Agreement

1. Introduction

<Introduction part (optional)>

2. Reason for Change

A solution for key issue 2 is proposed for the progress of the work.

3. Conclusions

<Conclusion part (optional)>

4. Proposal

It is proposed to agree the following changes to 3GPP TR 24.821 V0.1.0.

* * * First Change * * * *

## 6.x	Solution X

### 6.x.1	Target key issue

This solution addresses key issue #2.

### 6.x.1	Solution description

The salient features of the solution are as follows.

a)	How the UE determines which PLMN(s) can be selected in determined country of its physical location (if it is determined that the UE is not in an international area)

The mapping (a country to one or more MCCs) information provisioned in the UE is used to determine the PLMN(s) which can be selected from the determined country. How to provision this information to the UE is outside the scope of 3GPP in this solution.

Editor's note:	It is FFS if the coding of the countries needs to be defined by 3GPP.

b)	What information could be available to the UE to help in selecting, in a given country, a PLMN that meets the LI requirements of that country

The mapping (a country to one or more MCCs) information provisioned in the UE. The mapping from an MCC to PLMNs is straightforward.

c)	What modifications are needed, if any, to the PLMN selelction procedure to take the LI requirement into account

Key differences compared to the current PLMN selection procedure are as follows.

1)	The UE prioritizes PLMNs with the MCC(s) corresponding to the country of its physical location or the MCC(s) recommended by the network. The MCC(s) recommended by the network shall be used only during the PLMN selection followed by the reception of the MCC(s).

2)	If there is no PLMN with the MCC(s) corresponding to the country of its physical location or the MCC(s) recommended by the network, the UE can select a PLMN with an MCC which is not equal to any of the MCC(s) which correspond to the country of its physical location or have been recommended by the network. In this case, the UE turns into a "particular" state (e.g. the limited service state, a new state) because emergency services can be impacted.

NOTE:	A UE in the "particular" state is a UE which has selected a PLMN with the MCC not corresponding to the country of the UE's physical location because the UE was not able to select a PLMN with the MCC corresponding to the country of the UE's physical location. Therefore, the key difference to a UE in the normal state is that a UE in the "particular" state has a limitation in regulatory services and for a UE in the "particular" state the network does not send the list of recommended MCCs.

Editor's note:	It is FFS if the UE selecting a shared/global PLMN ID should be in the "particular" state.

Editor's note:	Priority between a forbidden PLMN with an MCC corresponding to the country of its physical location and a PLMN with an MCC not corresponding to the country of tis physical location is FFS.

3)	While a UE is in not only in a VPLMN but also in the (E)HPLMN, if the UE detects change in the country of its present location, the UE needs to attempt to operate as specified in bullets 1) and 2) in addition to periodically scanning a higher priority PLMN with the same MCC as the currently serving PLMN's MCC.

### 6.x.3	Impacts to existing procedures due to the solution

UE:

-	The UE prioritizes PLMNs with the MCC(s) corresponding to the country of its physical location or the MCC(s) recommended by the network.

-	The "particular" state needs to be supported.

Network:

-	The network should be able to handle a UE in the "particular state".