3GPP TSG-CT WG1 Meeting #127-e	C1-20xxxx

# Electronic meeting; 13-20 November 2020

Source:	Nokia, Nokia Shanghai Bell

Title:	Solution for key issue 4

Spec:	3GPP TR 24.821 V0.1.0

Agenda item:	17.2.4

Document for:	Agreement

1. Introduction

<Introduction part (optional)>

2. Reason for Change

A solution for key issue 4 is proposed for the progress of the work.

3. Conclusions

<Conclusion part (optional)>

4. Proposal

It is proposed to agree the following changes to 3GPP TR 24.821 V0.1.0.

* * * First Change * * * *

## 6.x	Solution X

### 6.x.1	Target key issue

This solution addresses key issue #4.

### 6.x.1	Solution description

The salient features of the solution are as follows.

a)	What modifications are needed to the PLMN selection procedure to handle shared/global PLMN IDs

No change is required in addition to modifications to the PLMN selelction procedure to take the LI requirement into account (which is addressed in key issues #2) because in order to satsfy the LI requirement addressed in the key issue, a PLMN of the country of the UE's location needs to be prioritized. If a UE cannot determine the country of its physical location (due to its capability limitation or its physical location in an international area) or a PLMN belonging to the country of the UE's physical location is not available, the UE can select a PLMN according to the legacy algorithm. In this case, selection of a shared/global PLMN ID is not prohibited.

b)	Should these changes also apply to the legacy PLMN selection procedure

No.

c)	What information could be available to aid in handling shared/global PLMN IDs

Existing lists can be used. For example, "User Controlled PLMN Selector with Access Technology" can be used to (de)prioritize selecting a shared/global PLMN ID if a UE cannot determine the country of its physical location or a PLMN belonging to the country of the UE's physical location is not available.

d)	How to accommodate LI requirements when handling shared/global PLMN IDs

A shared/global PLMN ID can be selected if:

-	a UE cannot determine the country of its physical location (due to its physical location in an international area); or

-	a PLMN belonging to the country of the UE's physical location is not available or allowable (i.e. if the UE is in a situation where the LI requirement cannot be fulfilled).

Or even if:

-	the UE can determine the country of its physical location; and

-	a PLMN belonging to the country of the UE's physical location is available and allowable;

if one or more shared/global PLMN IDs are allowed to be selected from the country (which can be known from the mapping information discussed in key issue #2) according to the LI requirement, a shared/global PLMN IDs can be selected.

### 6.x.3	Impacts to existing procedures due to the solution

No impact.