3GPP TSG-CT WG1 Meeting #127-e	C1-20xxxx

# Electronic meeting; 13-20 November 2020											(was C1-207223)

Source:	Qualcomm Incorporated

Title:	Addition of Key Issue on prevention of signalling overload by returning UEs in PLMN previously with Disaster Condition for MINT

Spec:	3GPP TR 24.xxx v0.0.0

Agenda item:	17.1.2

Document for:	Agreement

1. Introduction

This contribution proposes to add Key Issue #y: “Prevention of signalling overload by returning UEs in PLMN previously with Disaster Condition” to MINT TR 24.xxx.

2. Reason for change

In LS SP-200880, SA directed CT1 to have a Rel-17 Study Item on MINT and specifically requested CT1 to study “how to avoid “returning UEs” overloading the PLMN that had earlier failed”. A corresponding Key Issue needs to be added to TR 24.xxx.

3. Proposal

It is proposed to agree the following changes to 3GPP TR 24.xxx v0.0.0.

* * * First Change * * * *

## 5.Y	Key Issue #<y>: Prevention of signalling overload by returning UEs in PLMN previously with Disaster Condition

### 5.Y.1	Description

According to 3GPP TS 22.261 [a] subclause 6.31.2.2:

The 3GPP system shall be able to provide efficient means for a network to inform Disaster Inbound roamers that a Disaster Condition is no longer applicable.

And according to 3GPP TS 22.261 [a] subclause 6.31.2.3:

Disaster Inbound Roamers shall perform network reselection when a Disaster Condition has ended.

This means that when a Disaster Condition is no longer applicable, all UEs of the PLMN that was previously with Disaster Condition which are currently served by another PLMN and are currently in 5GMM-IDLE mode will perform PLMN reselection and return to the PLMN that was previously with Disaster Condition. These UEs will then attempt to register to obtain service. This could cause a large number of UEs to migrate from PLMNs without Disaster Condition back to the PLMN which was previously with Disaster Condition, and attempt registration at around the same time, leading to signalling overload in the PLMN previously with Disaster Condition due to the massive return of UEs. Consequently, means are needed to prevent signalling overload in the PLMN previously with Disaster Condition. This is also reflected in the following service requirement of 3GPP TS 22.261 [a] subclause 6.31.2.3:

The 3GPP system shall minimize congestion caused by Disaster Roaming.

The following question is expected to be studied within this Key Issue:

-	How to stagger the return of UEs to the PLMN previously with Disaster Condition, so as to spread out registration attempts over time and keep the number of UEs attempting to register simultaneously within a manageable limit.

* * * End of Changes * * * *