# 3GPP TSG CT WG1 Meeting 127-e	TDoc C1-20xxxx

# Electronic meeting, 13-20 November 2020

Title:	AMF providing UE's acknowledgement for successful reception of the SOR information to UDM

Release:	Rel-15, Rel-16

Work Item:	5GS_Ph1-CT

Source:	3GPP TSG CT WG1

To:	3GPP TSG SA WG3

Cc:	3GPP TSG CT WG4

Contact person:	Lufeng.Han

Lufeng.han@vivo.com

Send any reply LS to:	3GPP Liaisons Coordinator, mailto:3GPPLiaison@etsi.org

Attachments:	none

# 1	Overall description

CT1 identified that SA3 has approved a TS 33.501 Release 15 CR#0943 (S3-202248) and the corresponding Release 16 mirror CR#0944 (S3-202249) that when a transparent container with the SoR-MAC-IUE was received in the Registration Complete message the AMF shall include the SOR-MAC-Iue but not the transparent container in Nudm_SDM_Info request message that is sent to the UDM, which does not comply to the stage 2 requirements in TS 23.122 where the AMF is required to pass the received SOR transparent container to the UDM.

Quote from TS 23.122 V15.7.0 subclause C.2 and C.3:

"…

10)	The AMF to the UDM: If an SOR transparent container is received in the REGISTRATION COMPLETE message, the AMF uses the Nudm_SDM_Info service operation to provide the received SOR transparent container to the UDM. If the HPLMN decided that the UE is to acknowledge the successful security check of the received steering of roaming information in step 4, the UDM verifies that the acknowledgement is provided by the UE as specified in 3GPP TS 33.501 [66];

…"

"…

5)	The AMF to the UDM: If the UL NAS TRANSPORT message with an SOR transparent container is received, the AMF uses the Nudm_SDM_Info service operation to provide the received SOR transparent container to the UDM. If the HPLMN decided that the UE is to acknowledge successful security check of the received list of preferred PLMN/access technology combinations in step 1, the UDM verifies that the acknowledgement is provided by the UE.

…"

CT1 has preference for updating TS°33.501 on this part to align with the stage 2 requirement in TS 23.122 to address this misalignment.

# 2	Actions

To 3GPP TSG SA WG3

ACTION: 	CT1 kindly asks SA3 to take the above information into account and update TS°33.501 (Release 15 and Release 16) on this part to align with the stage 2 requirement, if deemed appropriate.

# 3	Dates of next TSG CT WG1 meetings

TSG CT WG1 Meeting 127-bis-e (electronic)	25-29 January 2021

TSG CT WG1 Meeting 128-e (electronic)	25 February - 05 March 2021