3GPP TSG-CT WG1 Meeting #127-e	C1-207648

# Electronic meeting; 13-20 November 2020

Source:	LG Electronics, Ericsson

Title:	New Key Issues for MINT: Indication of accessibility from other PLMNs not subject to disaster to the UE

Spec:	3GPP TR 24.xxx (draft)

Agenda item:	17.1.2

Document for:	Agreement

1. Reason for Change

This Key issue will try to resolve the following service requirements in TS 22.261

The 3GPP system shall be able to provide a resource efficient means for a PLMN to indicate to potential Disaster Inbound Roamers whether they can access the PLMN or not.

A corresponding Key Issue needs to be added to TR 24.xxx.

2. Proposal

It is proposed to agree the following new key issue to 3GPP TR 24.xxx v0.0.0.

* * * First Change (new)* * * *

## 5.XC	Key Issue #XC: Indication of accessibility from other PLMNs without Disaster Condition to the UE

### 5.XC.1	Description

According to 3GPP TS 22.261 [r22261] subclause 6.31.2.3:

The 3GPP system shall be able to provide a resource efficient means for a PLMN to indicate to potential Disaster Inbound Roamers whether they can access the PLMN or not.

When a Disaster Condition applies to a particular PLMN or PLMNs, one or more PLMNs in the same country may be able to provide Disaster Roaming service to the UEs of a PLMN with Disaster Condition. In this case, the PLMN providing Disaster Roaming shall indicate that it can accommodate the Disaster Inbound Roamers from a PLMN with Disaster Condition.

The following questions are expected to be studied within this Key Issue:

-	Which PLMN(s) are responsible for indicating their accesibility to Disaster Inbound Roamers;

-	How other PLMN(s) than the PLMN with Disaster Condition indicate that they can accommodate Disaster Inbound Roamer; and

-	What information can be provided to potential Disaster Inbound Roamers.

NOTE:	The interactions between this Key Issue and the Key Issue #XG (Prevention of signalling overload in PLMNs without Disaster Condition) need to be considered, since preventing UEs from overloading a PLMN without Disaster Condition could have an impact on whether and how the PLMN indicates that it can accept Disaster Inbound Roamers.

* * * End Change * * * *