3GPP TSG-CT WG1 Meeting #127-e	C1-207xxc

# Electronic meeting; 13-20 November 2020

Source:	LG Electronics

Title:	New Key Issues for MINT: Notification of disaster condition to the UE

Spec:	3GPP TR 24.xxx (draft)

Agenda item:	17.1.2

Document for:	Agreement

1. Reason for Change

This Key issue will try to resolve the following service requirements in TS 22.261

The 3GPP system shall enable UEs to obtain information that a Disaster Condition applies to a particular PLMN or PLMNs.

NOTE:  If a UE has no coverage of its HPLMN, then obtains information that a Disaster Condition applies to the UE's HPLMN, the UE can register with a PLMN offering Disaster Roaming service.

The 3GPP system shall provide means to enable that a Disaster Condition applies to UEs of a specific PLMN.

A corresponding Key Issue needs to be added to TR 24.xxx.

2. Proposal

It is proposed to agree the following changes to 3GPP TR 24.xxx v0.0.0.

* * * First Change (new)* * * *

## 5.XA	Key Issue #XA: Notification of Disaster Condition to the UE

### 5.XA.1	Description

According to 3GPP TS 22.261 [r22261] subclause 6.31.2.2:

The 3GPP system shall enable UEs to obtain information that a Disaster Condition applies to a particular PLMN or PLMNs.

NOTE:  If a UE has no coverage of its HPLMN, then obtains information that a Disaster Condition applies to the UE's HPLMN, the UE can register with a PLMN offering Disaster Roaming service.

According to 3GPP TS 22.261 [r22261] subclause 6.31.2.3:

The 3GPP system shall provide means to enable that a Disaster Condition applies to UEs of a specific PLMN.

When a Disaster Condition applies to a PLMN or PLMNs in an area, a UE is located in the area, and the PLMN is HPLMN of the UE or was selected by the UE, then the UE shall be able to obtain information that the Disaster Condition applies to the PLMN.

NOTE:	The interactions between this Key Issue and the Key Issue #XG (Prevention of signalling overload in PLMNs without Disaster Condition) need to be considered, since preventing UEs from overloading the PLMN previously with Disaster Condition could have an impact on how the PLMNs without Disaster Condition are notified that the Disaster Condition no longer applies.

The following questions are expected to be studied within this Key Issue:

-	How to deliver the information on the Disaster Condition of a PLMN in an area to the UE located in the area;

-	Which network functions or entities are involved for the delivery of the information

-	Which PLMN(s) are responsible for the delivery of the information; and

-	What kind of information should be delivered to the UE.

* * * End Change * * * *