3GPP TSG-CT WG1 Meeting #127-e	C1-207xxd

# Electronic meeting; 13-20 November 2020

Source:	LG Electronics

Title:	New Key Issues for MINT: Notification of applicability on disaster condition to other PLMNs not subject to disaster

Spec:	3GPP TR 24.xxx (draft)

Agenda item:	17.1.2

Document for:	Agreement

1. Reason for Change

This Key issue will try to resolve the following service requirements in TS 22.261

Subject to regulatory requirements or operator’s policy, the 3GPP system shall support a PLMN operator to be made aware of the failure or recovery of other PLMN(s) in the same country when the Disaster Condition is applies, or when the Disaster Condition is not applicable.

The 3GPP system shall support means for a PLMN operator to be aware of the area where Disaster Condition applies.

A corresponding Key Issue needs to be added to TR 24.xxx.

2. Proposal

It is proposed to agree the following changes to 3GPP TR 24.xxx v0.0.0.

* * * First Change (new)* * * *

## 5.XB	Key Issue #XB: Notification of applicability on disaster condition to other PLMNs not subject to disaster

### 5.XB.1	Description

According to 3GPP TS 22.261 [r22261] subclause 6.31.2.2:

Subject to regulatory requirements or operator’s policy, the 3GPP system shall support a PLMN operator to be made aware of the failure or recovery of other PLMN(s) in the same country when the Disaster Condition is applies, or when the Disaster Condition is not applicable.

The 3GPP system shall support means for a PLMN operator to be aware of the area where Disaster Condition applies.

When a Disaster Condition applies to a particular PLMN or PLMNs, the PLMN(s) in the same country not subject to disaster shall be notified that Disaster Condition applies to PLMN(s) or Disaster Condition no longer applies. Also as per service requirement quoted above, the PLMN(s) in the same country can be aware of the area where Disaster Condition applies.

The following questions are expected to be studied within this Key Issue:

-	How to deliver the information on the Disaster Condition to the neighboring PLMNs not subject to disaster;

-	Who or which entity decides the Disaster Condition;

-	Which PLMNs are subject to recevie the information on Disaster Condition; and

-	How to provide information on the area where Disaster Condition applies.

NOTE:	The interactions between this Key Issue and the Key Issue #XH (Prevention of signalling overload by returning UEs in PLMN previously subject to disaster) need to be considered, since preventing UEs from overloading a PLMN not subject to disaster could have an impact on what kind of information should be delivered to the UE.

* * * End Change * * * *