3GPP TSG-CT WG1 Meeting #128-e	C1-211124

# Electronic meeting; 25 February – 5 March 2021

Source:	Samsung, AT&T, Qualcomm Incorporated, Deutsche Telekom, Intel, Ericsson

Title:	Eecs_ServiceProvisioning API

Spec:	3GPP TS 24.558 v0.0.0

Agenda item:	17.2.10

Document for:	Agreement

1. Introduction

This pCR provides details for Eecs_ServiceProvisioning API.

2. Reason for Change

The Eecs_ServiceProvisioning API is defined in clause 8.3.3.4 of 3GPP TS 23.558. It is reqired to implement the API in stage#3 specification.

3. Proposal

It is proposed to agree the following changes to 3GPP TS 24.558 v0.0.0.

* * * First Change * * * *

### B.1.3	Eecs_ServiceProvisioning API

#### B.1.3.1	API URI

The request URI used in each HTTP request from the EEC towards the ECS shall have the structure as defined in clause 7.5 with the following clarifications:

-	The <apiName> shall be "ecs-serviceprovisioning".

-	The <apiVersion> shall be "v1".

-	The <apiSpecificResourceUriPart> shall be set as described in clause B.1.3.2.

#### B.1.3.2	Resources

##### B.1.3.2.1	Overview

Figure B.1.3.2.1-1: Resource URI structure of the Eecs_ServiceProvisioning API

Editor’s Note: Inclusion of {ueId} in the URL path before the {eecId} is TBD and requires further direction from SA3. In the absence of {ueId} in the URL path, the need for having {eecId} in the path is questionable.

Table B.1.3.2.1-1 provides an overview of the resources and applicable HTTP methods.

Table B.1.3.2.1-1: Resources and methods overview

| Resource name | Resource URI | HTTP method or custom operation | Description |
| --- | --- | --- | --- |
| Provisioning Information | {apiRoot} /ecs-serviceprovisioning/v1 /{eecId}/provisioningInfo | fetch (POST) | Provide the information required by the UE to access the edge services. |

##### B.1.3.2.2	Resource: Provisioning Information

###### B.1.3.2.2.1	Description

This resource represents provisioning information required by the UE to access the edge services.

###### B.1.3.2.2.2	Resource Definition

Resource URI: {apiRoot}/ecs-serviceprovisioning/v1/{eecId}/provisioningInfo

This resource shall support the resource URI variables defined in table B.1.3.2.2.2-1.

Table B.1.3.2.2.2-1: Resource URI variables for this resource

| Name | Definition |
| --- | --- |
| apiRoot | See clause 7.5 |

###### B.1.3.2.2.3	Resource Standard Methods

None.

###### B.1.3.2.2.3		Resource Custom Operations

Editor’s Note: The resource Custom Operations for Eecs_ServiceProvisioning API is FFS.

#### B.1.3.3	Custom Operations without associated resources

None.

#### B.1.3.3	Notifications

None.

#### B.1.3.5	Data Model

Editor’s Note: The data model for Eecs_ServiceProvisioning API is FFS.

#### B.1.3.6	Error Handling

Editor’s Note: The error handling for Eecs_ServiceProvisioning API is FFS.

#### B.1.3.7	Feature negotiation

Editor’s Note: The Feature negotiation for Eecs_ServiceProvisioning API is FFS.

* * * End of Change * * * *

# Comments

Changes over changes will be removed before submission