3GPP TSG-CT WG1 Meeting #128-e	C1-211123

# Electronic meeting; 25 February – 5 March 2021

Source:	Samsung, AT&T, Qualcomm Incorporated, Deutsche Telekom, Intel

Title:	Eees_EASDiscovery API

Spec:	3GPP TS 24.558 v0.0.0

Agenda item:	17.2.10

Document for:	Agreement

1. Introduction

This pCR provides details for Eees_EASDiscovery API.

2. Reason for Change

The Eees_EASDiscovery API is defined in clause 6.5.4 of 3GPP TS 23.558. It is reqired to implement the API in stage#3 specification.

3. Proposal

It is proposed to agree the following changes to 3GPP TS 24.558 v0.0.0.

* * * First Change * * * *

## 6.x	Eees_EASDiscovery API

### 6.x.1	API URI

The request URI used in each HTTP request from the EEC towards the EES shall have the structure as defined in clause 6.1.5 with the following clarifications:

-	The <apiName> shall be "ees-easdiscovery".

-	The <apiVersion> shall be "v1".

-	The <apiSpecificResourceUriPart> shall be set as described in clause 6.x.2.

### 6.x.2	Resources

#### 6.x.2.1	Overview

Figure 6.x.2.1-1: Resource URI structure of the Eees_EASDiscovery API

Table 6.x.2.1-1 provides an overview of the resources and applicable HTTP methods.

Table 6.x.2.1-1: Resources and methods overview

| Resource name | Resource URI | HTTP method or custom operation | Description |
| --- | --- | --- | --- |
| EAS Discovery Information | {apiRoot} /ees-easdiscovery/v1 /easDiscoveryInfo | fetch (POST) | A collection of EAS information. |

#### 6.x.2.2	Resource: EAS Discovery Information

##### 6.x.2.2.1	Description

This resource represents a collection of registered EAS information on a EES.

##### 6.x.2.2.2	Resource Definition

Resource URI: {apiRoot}/ees-easdiscovery/v1/easDiscoveryInfo

This resource shall support the resource URI variables defined in table 6.x.2.2.2-1.

Table 6.x.2.2.2-1: Resource URI variables for this resource

| Name | Definition |
| --- | --- |
| apiRoot | See clause 6.1.5 |

##### 6.x.2.2.3	Resource Standard Methods

None.

##### 6.x.2.2.4		Resource Custom Operations

Editor’s Note: The resource Custom Operations for Eecs_ServiceProvisioning API is FFS.

### 6.x.3	Custom Operations without associated resources

None.

### 6.x.4	Notifications

None.

### 6.x.5	Data Model

Editor’s Note: The data type definitions for Eees_EASDiscovery API is FFS.

### 6.x.6	Error Handling

Editor’s Note: The error handling for Eees_EASDiscovery API is FFS.

### 6.x.7	Feature negotiation

Editor’s Note: The Feature negotiation for Eees_EASDiscovery API is FFS.

* * * End of Change * * * *