3GPP TSG-CT WG1 Meeting #128-e	C1-211102

# Electronic meeting; 25 February – 5 March 2021

Source:	Samsung, AT&T

Title:	Clasue 4 - Overview

Spec:	3GPP TS 24.558 v0.0.0

Agenda item:	17.2.10

Document for:	Agreement

1. Introduction

This pCR provides overview of the specification 3GPP TS 24.558

2. Reason for Change

Overview claues is a mandaotry as per the TS template, so it is necessary to provide overview of the specification.

3. Proposal

It is proposed to agree the following changes to 3GPP TS 24.558 v0.0.0.

* * * First Change * * * *

# 4	Overview

3GPP TS 23.558 [r23558] has specified the application layer architecture, requirements, procedures, information flows and the APIs, in order to support the edge applications over the 3GPP systems. Various features are defined to ensure the efficient use and deployment of edge applications, some of which include, registration, discovery, service provisioning, capability exposure and support for service continuity.

The present document specifies the APIs in detail, needed to support the services offered by EES over EDGE-1 interface for enabling the edge applications over 3GPP network.

Editor’s note: It is FFS whether EASDiscovery service (over EGDE-1) and TargetEASDiscovery service (over EDGE-3) can be unified or not. The structure and content of this specification may require major updates depending on it.

* * * End of Change * * * *

# Comments

Changes over change will be removed before submission