3GPP TSG-CT WG1 Meeting #128-e	C1-2XXXX

Electronic meeting, 25 February – 5 March 2021	was C1-211049

| CR-Form-v12.1 |
| --- |
| CHANGE REQUEST |
|  | 27.007 | CR | 0720 | rev | 1 | Current version: | 17.0.0 |  |
| For HELP on using this form: comprehensive instructions can be found at http://www.3gpp.org/Change-Requests. |

| Proposed change affects: | UICC apps |  | ME | X | Radio Access Network |  | Core Network |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

| Title: | Clarification in scope of “nwimsvops_n3gpp “ parameter in +CIREP AT command |
| --- | --- |
| Source to WG: | MediaTek Inc |
| Source to TSG: | C1 |
| Work item code: | TEI17 |  | Date: | 2021-02-17 |
| Category: | F |  | Release: | Rel-17 |
|  | Use one of the following categories: F (correction) A (mirror corresponding to a change in an earlier release) B (addition of feature), C (functional modification of feature) D (editorial modification) Detailed explanations of the above categories can be found in 3GPP TR 21.900. | Use one of the following releases: Rel-8 (Release 8) Rel-9 (Release 9) Rel-10 (Release 10) Rel-11 (Release 11) ... Rel-15 (Release 15) Rel-16 (Release 16) Rel-17 (Release 17) Rel-18 (Release 18) |
| Reason for change: | In section “8.64 “ the AT command +CIREP is covered. For this AT command the possible responses mentioned are “+CIREP: <reporting>,<nwimsvops>,<nwimsvops_n3gpp> “. While this AT command is generic and applicable for both EPS and 5GS, however the response “nwimsvops_n3gpp “ is possible only in case of 5GS and not in case of EPS. This is because the VoPS indication for non3GPP is defined only for 5GS and not for EPS as per 24.301/24.501. Via this tDoc, we are adding this clarification in the scope of “nwimsvops_n3gpp “. |
| Summary of change: | In Section 8.64 the applicability of “nwimsvops_n3gpp “is made limited to 5GS in accordance with specifications 24.501/24.301. |
| Consequences if not approved: | Will result in wrong UE implementation in aplicability of parameter “nwimsvops_n3gpp “. |
| Clauses affected: | 8.64 |
|  | Y | N |  |  |
| Other specs |  | X | Other core specifications | TS/TR ... CR ... |
| affected: |  | X | Test specifications | TS/TR ... CR ... |
| (show related CRs) |  | X | O&M Specifications | TS/TR ... CR ... |
| Other comments: |  |
| This CR's revision history: |  |

##### ***** Next change *****

## 8.64	IMS network reporting +CIREP

Table 8.64-1: +CIREP parameter command syntax

| Command | Possible response(s) |
| --- | --- |
| +CIREP=[<reporting>] |  |
| +CIREP? | +CIREP: <reporting>,<nwimsvops>,<nwimsvops_n3gpp> |
| +CIREP=? | +CIREP: (list of supported <reporting>s) |

Description

Set command enables or disables reporting of PS to CS Single Radio Voice Call Continuity (SRVCC), PS to CS Single Radio Video Call Continuity (vSRVCC) handover information and CS to PS Single Radio Voice Call Continuity (see 3GPP TS 24.237 [91]), of IMS Voice Over PS sessions (IMSVOPS) indicator information and of IMS Voice Over PS sessions over non-3GPP (IMSVOPS-N3GPP) indicator information, by the following unsolicited result codes:

+CIREPI: <nwimsvops>, <nwimsvops_n3gpp> IMS Voice Over PS sessions (IMSVOPS) supported indication from the network and IMS Voice Over PS sessions over non-3GPP (IMSVOPS-N3GPP) supported indication.

+CIREPH: <srvcch> Provides PS to CS SRVCC, PS to CS vSRVCC and CS to PS SRVCC handover information.

Read command returns the status of result code presentation and the IMSVOPS supported indication.

Test command returns supported values as a compound value.

Defined values

<reporting>: integer type. Enables or disables reporting of changes in the IMSVOPS and the IMSVOPS-N3GPP supported indications received from the network and reporting of PS to CS SRVCC, PS to CS vSRVCC and CS to PS SRVCC handover information.

0	Disable reporting

1	Enable reporting

<nwimsvops>: integer type. Gives the last IMS Voice Over PS sessions (IMSVOPS) supported indication received from network.

0	IMSVOPS support indication is not received from network, or is negative.

1	IMSVOPS support indication as received from network is positive.

<nwimsvops_n3gpp>: integer type. Gives the last IMS Voice Over PS sessions over non-3GPP (IMSVOPS-N3GPP) supported indication received from network. The parameter is only provided in a 5GS system.

0	IMSVOPS-N3GPP support indication is not received from network, or is negative.

1	IMSVOPS-N3GPP support indication as received from network is positive.

<srvcch>: integer type. PS to CS SRVCC, PS to CS vSRVCC and CS to PS SRVCC handover information.

0	PS to CS SRVCC handover has started in the CS domain ("Handover Command" indicating PS to CS SRVCC received).

1	PS to CS SRVCC handover successful ("Handover Complete" sent).

2	PS to CS SRVCC or PS to CS vSRVCC handover cancelled ("Handover Failure" sent).

3	PS to CS SRVCC or PS to CS vSRVCC handover, general non-specific failure.

4	PS to CS vSRVCC handover has started in the CS domain ("Handover Command" indicating vSRVCC received).

5	PS to CS vSRVCC handover successful ("Handover Complete" sent).

6	CS to PS SRVCC handover has started in the PS domain ("Handover Command" indicating CS to PS SRVCC received).

7	CS to PS SRVCC handover cancelled ("Handover Failure" sent).

8	CS to PS SRVCC handover, general non-specific failure.

9	CS to PS SRVCC handover successful ("Handover Complete" sent).

NOTE 1:	Value 3 and 8, general non-specific failure, might be used e.g. in the case of handover cancellation as specified in 3GPP TS 24.301 [83] subclause 6.6.2.

NOTE 2:	The naming of SRVCC and vSRVCC handover information values is different from the naming of corresponding NAS session management notifications.

NOTE 3:	PS to CS SRVCC support also includes the support of 5G-SRVCC from NG-RAN to UTRAN as specified in 3GPP TS 23.216 [171] subclause 6.5.4.

Implementation

Optional.