3GPP TSG-CT WG1 Meeting #128-e	C1-211053

# Electronic meeting; 25th Feb-5th March 2021

Source:	Huawei, HiSilicon

Title:	EN resolution of assigning service area for Solution #19 KI#4.

Spec:	3GPP TR 24.811

Agenda item:	17.2.9

Document for:	Agreement

1. Introduction

This pCR attempts to resolve the following editors note for the solution #19 for KI #4

Editor's note: It is FFS on how the PLMN assign service area based on the disaster area.

Assigning service area is removed as a solution.

2. Reason for Change

Editors note need to be resolved.

3. Conclusions

4. Proposal

It is proposed to agree the following changes to 3GPP TR 24.811.

* * * First Change * * * *

### 6.19.2	Solution description

To solve the problem the UE needs to differentiate the registration request due to disaster roaming and a normal registration request. So The UE needs to use a new registration request type in the registration request message. This will help the NW identify that the UE is performing a registration followed by disaster condition. The NW may accept the registration request from such a UE if the network supports disaster roaming in that area from the previously served PLMN of the UE. .

Editor's note: It is FFS on how AMF uses this information towards AUSF for the authentication of the UE.

- The registration type is used by the UE only if it has detected a disaster condition and needs to move away from the serving PLMN.

NOTE:	PLMN that supports disaster roaming can accept the registration request from the UE if the UE indicates that it is performing registration request due to a disaster condition and if the PLMN supports disaster roaming from the previously served PLMN of that UE in that area.

Editor's note: It is FFS on how to make sure that an attacker UE does not misuse the new registration type request to get access to a PLMN where it is not allowed to access.

- Visiting NW can also assign the tracking areal list (TAI list) based on the area where the disaster has happened. This also has the advantage that the UE will perform a mobility and registration update procedure as soon as UE moves out of the area.

* * * End of Change * * * *