3GPP TSG-CT WG1 Meeting #128-e	C1-211060

# Electronic meeting; 25th Feb-5th March 2021

Source:	Huawei, HiSilicon

Title:	EN resolution for considering CAG cells for Solution #24 KI#5.

Spec:	3GPP TR 24.811

Agenda item:	17.2.9

Document for:	Agreement

1. Introduction

This pCR attempts to discuss the following editors note for the solution #24 for KI #5. It is decided that an LS will be sent to SA1 to clarfiy the situation. It is updated accordingly.

Editor's note: For a UE supporting CAG, it is FFS how the CAG cells that are not in the Allowed CAG list of the UE are considered for disaster roaming.

2. Reason for Change

Editors note need to be resolved.

3. Conclusions

4. Proposal

It is proposed to agree the following changes to 3GPP TR 24.811.

* * * First Change * * * *

### 6.24.1	General

The solution aims at solving the below study item in the key issue #5

How the UE selects a PLMN if it is determined that a "Disaster Condition" applies;

a)	If the UE determines that a "Disaster Condition" applies as described in Key Issue #1 "Notification of Disaster Condition to the UE", then how to update PLMN selection procedure so that the UE avoids selecting the PLMN with "Disaster Condition".

b)	How the UE handles the list of "forbidden PLMNs" when selecting a PLMN indicating accessibility for the UE in the bullet a).

Once the UE detects "Disaster Condition" based on the solution for key issue #1, UE shall perform a PLMN selection and shall consider the list of “List of PLMNs to be used while in Disaster condition” in the PLMN selection. In the PLMN selection procedure, if the UE finds PLMN that is in the forbidden PLMN list, UE shall consider the forbidden PLMN also for PLMN selection if they are present in the “List of PLMNs to be used while in Disaster condition”. Forbidden PLMNs shall be considered in the same order in which they are present in the “List of PLMNs to be used while in Disaster condition”.

This is because the serving PLMN can arrange the PLMNs in a particular order to distribute the UEs equally among the PLMNs.

Editor's note: It is FFS on how the AMF of the serving PLMN arranges the PLMN in an order based on an area for equal distribution.

As long as the "Disaster Condition" is applicable, PLMNs in the forbidden list can be considered as available if they are present in the “List of PLMNs to be used while in Disaster condition” and if those PLMNs indicate that they support disaster roaming. Once the "Disaster Condition" is over, UE shall treat the PLMNs in the forbidden PLMN list as forbidden. Otherwise no need for any change for the forbidden PLMN list.

Editor's note: For a UE supporting CAG,  whether and how the CAG cells that are not in the Allowed CAG list of the UE are considered for disaster roaming is subject to SA1 decision.

* * * End of Change * * * *