3GPP TSG-CT WG1 Meeting #128-e	C1-211071

# Electronic meeting; 25th Feb-5th March 2021

Source:	Huawei, HiSilicon

Title:	EN resolution of considering disaster PLMN for PLMN selection Solution #24 KI#5.

Spec:	3GPP TR 24.811

Agenda item:	17.2.9

Document for:	Agreement

1. Introduction

This pCR attempts to resolve the following editors note for the solution #24 for KI #5

Editor's note: It is FFS whether the PLMN in disaster condition becoming available before the disaster condition is over is a valid scenario or not. If it is valid scenario, how to handle that PLMN in PLMN selection is also FFS.

In the CT1 meeting CT1#127_bis_e, it was discussed if the PLMN which is in disaster condition can become available temporarily and at the same time the disaster condition is not yet lifted.One such possible scenario is the RAN of the PLMN which went into disaster is up again for testing or maintainance but it is not yet ready to accept the users. In such case the PLMN can still be available in the air. But there exists already mechanism for testing RAN before they are available for commercial users. So it is possible to test the RAN with the existing mechanism.

2. Reason for Change

Editors note need to be resolved.

3. Conclusions

4. Proposal

It is proposed to agree the following changes to 3GPP TR 24.811.

* * * First Change * * * *

### 6.24.2	Solution description

Once the UE detects "Disaster Condition" based on the solution for key issue #1, UE performs PLMN selection as follows

- All the available PLMNs are sorted based on the PLMN selection algorithm defined in 3GPP TS 23.122 subclause 4.4.3.1.1 with the following changes

a)	UE arranges the available PLMNs in the order mentioned in i, ii, and iii in 4.4.3.1.1 based on the PLMN if they PLMNs fall in those categories.

b)	For bullets iv and v in 4.4.3.1.1, all the PLMNs that are present in the “List of PLMNs to be used while in Disaster condition” are sorted in the order in which they are present in “List of PLMNs to be used while in Disaster condition” if the PLMNs also indicate that they support disaster roaming. In normal scenario, these PLMNs are sorted in random order based on the signal strength. (bullets iv and v in 23.122 4.4.3.1.1).

Editor's note: It is FFS on whether the PLMNs from the “List of PLMNs to be used while in Disaster condition” needs to be given priority over other PLMNs in bullets iv and v in 4,4,3,1,1.

c)	UE selects the PLMN which is highest priority after following the above procedure.

-	If only forbidden PLMNs are available and if they are present in “List of PLMNs to be used while in Disaster condition” and if the PLMNs also indicate that they support disaster roaming, those PLMNs are selected in the order in which they are present in “List of PLMNs to be used while in Disaster condition”

* * * End of Change * * * *