3GPP TSG-CT WG1 Meeting #127bis-e	C1-211096

# Electronic meeting; 25-29 January 2021

Source:	Huawei, HiSilicon

Title:	Solution for KI#9 for Manual Selection

Spec:	3GPP TR 24.811

Agenda item:	17.2.9

Document for:	Agreement

1. Introduction

This pCR attempts to provide a UE-based solution for Key Issue #9 provided in TR 24.811

KI#9: Manual PLMN selection during disaster condition.

2. Reason for Change

Solution for KI#9

3. Conclusions

4. Proposal

It is proposed to agree the following changes to 3GPP TR 24.811.

* * * First Change * * * *

6.X	Solution X: Manual PLMN selection during disaster conditionWhen the disaster condition happens,  user will be denied service and the normal reaction can be to look for a the available networks and the PLMNs are presented to the usre. As per the current design the PLMNs that support disaster roaming, which are mostly forbidden PLMNs, will be indicated as forbidden to the users.

This gives a wrong impression to the user that the PLMN is forbidden and will not be chosen by the user. So it is porposed to study the following items for manual PLMN selection

- During Manual PLMN selection, how the upper layers are informed that some of the forbidden PLMNs support disaster roaming.

- What additional information need to be sent to the upper layers when the PLMNs that support disaster roaming are sent to upper layers.

- -	Should the PLMN which is under disaster condition be sent to the upper layers if it becomes available?

### 6.X.1	Solution description

To solve the key issues described in the above section, when the user performs a manual PLMN selection,

### if the UE finds PLMNs that support disaster roaming, the UE shall send an indication along with the PLMN ID that the PLMN supports disaster roaming to the upper layers. This will help the user understand that such a PLMN can actually provide service and can be selected.

### 6.X.3	Impacts on existing nodes and functionality

### None.

* * * End of Change * * * *