# 3GPP TSG CT WG1 Meeting 128-e	TDoc C1-210XXX

# Electronic meeting, 25 February – 5 March 2021

Title:	LS on broadcasting from other PLMN in case of Disaster Condition

Release:	Rel-17

Work Item:	FS_MINT-CT

Source:	CT1

To:	SA3

Cc:	RAN2

Contact person:	Sang Min Park

sangmin2.park@lge.com

Send any reply LS to:	3GPP Liaisons Coordinator, mailto:3GPPLiaison@etsi.org

Attachments:

# 1	Overall description

CT1 has studied on the CT aspects of MINT (Minimization of Service Interruption) based on the service requirements that SA1 had specified for Rel-17. The main objectives of the study are to investigate how the UE and the networks can minimize service interruptions when the serving PLMN has a service disruption due to a disaster. The results of the study are specified in TR 24.811.

Key aspects of the study are on how the UE is notified that a Disaster Condition applies to the serving PLMN and whether the other PLMNs can accept the inbound disaster roamers, and how to notify the UE that the Disaster Condition is no longer applicable to the PLMN previously with Disaster Condition. In order to resolve these questions, some of the proposed solutions in TR 24.811 suggest to use broadcast information from other PLMNs than the PLMN with Disaster Condition to deliver such information. However, there are some concerns on this approach that there can be potential security risks as there is no security protection on the broadcasted messages.

So CT1 would like to ask SA3:

1)	whether sending, receiving and utilizing broadcast information as being discussed in TR 24.811 from other PLMNs than the PLMN with Disaster Condition, which can be home PLMN or visited PLMN, pose any security risks; and

2)	if the answer to Q1 is yes, then what would be a way to avoid such a security risk?

# 2	Actions

To SA3

ACTION: 	CT1 kindly asks SA3 to provide answers to the questions above.

# 3	Dates of next TSG CT WG1 meetings

TSG CT WG1 Meeting 129-e (electronic)	19 - 23 April 2021

TSG CT WG1 Meeting 130-e (electronic)	20 – 28 May 2021