3GPP TSG-CT WG1 Meeting #132-e	C1-216293

# E-meeting, 11-15 October 2021

Title:	LS on GTP-C cause value used for UAS services

Response to:

Release:	Rel-17

Work Item:	ID_UAS

Source:	CT1

To:	CT4

Cc:	SA2

Contact person:	Lin Shu

shulin@huawei.com

Send any reply LS to:	3GPP Liaisons Coordinator, mailto:3GPPLiaison@etsi.org

Attachments:	None

# 1	Overall description

CT1 is implementing stage 2 requirements on UUAA-SM and C2 authorization in EPS as specified in TS 23.256 and has noticed that in following two cases the SMF+PGW-C needs to reject the PDN connectivity request:

- SMF+PGW-C determines that UUAA-SM is required but CAA-level UAV ID is not provided by the UE; and

- SMF+PGW-C determines that C2 authorization is required but CAA-Level UAV ID and C2 aviation payload are not provided by the UE.

To avoid MME impact, CT1 has agreed

- to re-use an existing NAS ESM cause value provided by the MME to the UE in the PDN CONNECTIVITY REJECT message; and

- UAS services related rejection information will be indicated in a PCO parameter (rather than NAS ESM cause) of the PDN CONNECTIVITY REJECT message.

Existing NAS ESM cause #29 "User authentication or authorization failed" and cause #31 "Request rejected, unspecified" have been identified as preferred in CT1.

However, CT1 noted that in the PDN connectivity reject handling, it is the SMF+PGW-C provides a GTP-C cause value to the MME via the S-GW. Then, the MME maps the received GTP-C cause value to an NAS ESM cause value sent to the UE based on the mapping Table C.1 in TS 29.274. Concluding which existing NAS ESM cause value to be re-used, depends also on the GTP-C cause selected.

CT1 would like to ask CT4 which GTP-C cause could be selected to ensure that the mapping Table C.1 in TS 29.274 enables the MME to use an existing NAS ESM cause for the above PDN connectivity reject handling and which existing NAS ESM cause value it will be mapped to.

# 2	Actions

To CT4

ACTION: 	3GPP CT1 kindly asks CT4 to answer above question.

# 3	Dates of next TSG CT WG1 meetings

CT1#132e	11th-15th October 2021	electronic meeting

CT1#133e	11th-19th November 2021	electronic meeting