3GPP TSG-CT WG1 Meeting #132-e	C1-216296

# E-meeting, 11-15 October 2021

Title:	LS on Enquires on Application Context Relocation (ACR) functionality

Response to:	N/A

Release:	Rel-17

Work Item:	EDGEAPP

Source:	3GPP CT WG1

To:	3GPP SA WG6, 3GPP CT WG3

Cc:	-

Contact person:	Christian Herrero-Veron

Christian.Herrero at Huawei.com

Send any reply LS to:	3GPP Liaisons Coordinator, mailto:3GPPLiaison@etsi.org

Attachments: 	none

# 1	Overall description

# CT1 would like to provide the following information with regards to the work on Application Context Relocation (ACR) functionality in order to develop the stage 3 design details:

# (1)	CT1 has analysed the stage 2 work in TS 23.558 on the ACR launching procedure and the selected T-EAS declaration procedure and identified that a single API can be used for launching ACR in all scenarios. Additionally, when analysing the ACR response message, this message seems not to be properly design from stage 3 perspective as all parameters are optional, and as for the ACR request message it seems that the UE identifier information element should be mandatory, and therefore:

# CT1 asks SA6 and CT3 if the use of a single API for the ACR launching and selected T-EAS declaration is fine. Also, CT1 believes that the UE identifier has to be always included in the ACR request in order to let the EES understand for which UE or which EEC is a received ACR request. Finally, CT1 believes that the ACR response should be enhanced so that not all parameters are optional.

# 2	Actions

To 3GPP SA WG6, 3GPP CT WG3

ACTION:	CT1 kindly ask SA6 and CT3 to provide their view on the information above in order to progress on the ACR work.

# 3	Dates of next TSG CT WG1 meetings

CT1#133-e	11th-19th November 2021	electronic meeting

CT1#133-bis-e	17th-21st January 2022	electronic meeting