3GPP TSG-CT WG1 Meeting #132-e	C1-21xxxx

# E-meeting, 11-15 October 2021

Title:	LS on PCF in case of SNPN with CH using AUSF/UDM for primary auth

Response to:	-

Release:	Rel-17

Work Item:	eNPN

Source:	CT1

To:	SA2

Cc:	CT3

Contact person:	Sung Hwan WON

sung.won@nokia.com

Send any reply LS to:	3GPP Liaisons Coordinator, mailto:3GPPLiaison@etsi.org

Attachments:	-

# 1	Overall description

CT1 has been working on the NAS layer protocol regarding the 5GS architecture for SNPN with CH using AUSF and UDM for primary authentication and authorization depicted in Figure 5.30.2.9.3-1 of 3GPP TS 23.501, which does not show a PCF in the CH domain.

CT1 agreed that a URSP can be pre-configured in a UE for each of the subscribed SNPN. In addition, CT1 is discussing:

- whether a URSP to be used in SNPNs only (in addition to a URSP for the use is PLMNs) should be pre-configured in a UE if the UE can access SNPNs using the PLMN subscription; and

- how a UE associates URSP signaled via an SNPN when the UE has accessed the SNPN using credentials from a CH which is a PLMN or an SNPN, i.e. whether the signaled URSP should be associated with the SNPN or the CH.

CT1 has not reached consensus on these two issues.

# 2	Actions

To RAN2

ACTION: 	CT1 respectfully asks SA2 to provide feedback to the issues identified above.

# 3	Dates of next TSG CT WG1 meetings

CT1#132e	11th-15th October 2021	electronic meeting

CT1#133e	11th-19th November 2021	electronic meeting