3GPP TSG-CT WG1 Meeting #132-e	C1-216295

# E-meeting, 11-15 October 2021

Title:	Reply LS on EPS support for IoT NTN in Rel-17

Response to:	(C1-215531/RP-212617) LS on EPS support for IoT NTN in Rel-17 from RAN

Response to:	(C1-215524/ R2-2109213) LS on supporting discontinuous coverage in IoT NTN

Release:	Rel-17

Work Item:	LTE_NBIOT_eMTC_NTN, IoT_SAT_ARCH_EPS

Source:	CT1

To:	SA2, RAN2, CT, RAN, SA

Cc:	CT4, RAN3

Contact person:	Marko NIEMI

marko dot niemi at mediatek dot com

Send any reply LS to:	3GPP Liaisons Coordinator, mailto:3GPPLiaison@etsi.org

Attachments:	-

# 1	Overall description

CT1 would like to thank TSG RAN and RAN2 for their LS on EPS support for IoT NTN in Rel-17.

CT1 notes that TSG RAN (RAN2) is considering support for discontinuous coverage (incl. related impact on paging, (e)DRX, PSM, and PLMN search) as part of minimum essential functionality in RAN and RAN WGs and that TSG RAN is asking whether low-hanging fruit solutions are feasible at NAS relying on existing functionality or if TSG SA, SA2 should decide to introduce new functionality to support discontinuous coverage, to align with TSG SA, SA2.

Response:

CT1 132e discussed and thinks that for UE reachability existing NAS functionalities adjusting periodic update timer, mobile reachability timer, implicit detach timer, PSM and eDRX values would be sufficient for Rel-17 UEs and networks. However, CT1 also thinks that SA2 should discuss this topic and CT1 is fine to align the CT WID with SA2 decision.

CT1 notes that TSG RAN is emphasizing that work to support WUS in IoT NTN is ongoing, with RAN2 concluding the existing WUS mechanism can be reused without enhancement (except for minor enhancements if needed to support discontinuous coverage) and that they would therefore like to ask TSG SA, SA2, CT and CT1 to ensure WUS is not excluded

Response:

CT1 132e discussed and thinks that SA2 should first discuss on this topic. CT1 will align the CT WID with SA2 decision..

# 2	Actions

To CT, RAN, RAN2, SA, SA2

ACTION:	CT1 kindly asks groups to consider response given and provide feedback if necessary.

# 3	Dates of next TSG CT WG1 meetings

CT1#133e	11th-19th November 2021	electronic meeting