3GPP TSG-CT WG1 Meeting #132-e	C1-21abcd

# E-meeting, 11-15 October 2021

Title:	Reply LS on UAC enhancements for minimization of service interruption when disaster condition applies

Response to:	Reply LS R2-2109173 on UAC enhancements for minimization of service interruption when disaster condition applies

Release:	Rel-17

Work Item:	FS_MINT-CT

Source:	CT1

To:	RAN2

Cc:	-

Contact person:	Mikael Wass

mikael dot wass at ericsson dot com

-

Send any reply LS to:	3GPP Liaisons Coordinator, mailto:3GPPLiaison@etsi.org

Attachments:	None

# 1	Overall description

CT1 thanks RAN2 for the Reply LS on UAC enhancements for minimization of service interruption when disaster condition applies. To aid RAN2 in the selection between solutions #38 and #40, CT1 would like to provide the following feedback on the two questions asked in the Reply LS.

Q1: whether MINT UE should be independently configured for Access Identity 3 for each Access Category (compared to Access Identity 0)?

Answer 1: The barring factors to use with Access Identity 3 are indicated separately per Access Category. For solution #38 the RAN provides a set of barring factors specifically for Access Identity 3, and for solution #40, RAN provides a set of barring factors which offsets the legacy barring factors.

Q2: whether access control for Access Identity 3 applies both: barring factor and barring time?

Answer 2: For both solution #38 and solution #40, access control for Access Identity 3 applies specific barring factors only.

# 2	Actions

To RAN2

ACTION: 	CT1 asks RAN2 group to take the information above into account for the decision on selecting solution #38 or #40 for normative specification update.

# 3	Dates of next TSG CT WG1 meetings

CT1#132e	11th-15th October 2021	electronic meeting

CT1#133e	11th-19th November 2021	electronic meeting