3GPP TSG-CT WG1 Meeting #132-e	C1-21abcd

# E-meeting, 11-15 October 2021

Title:	LS on Slice list and priority information for cell reselection

Response to:	LS R2-2108928 on Slice list and priority information for cell reselection from RAN2

Release:	Rel-17

Work Item:	NR_Slice-Core

Source:	CT1

To:	RAN2 and SA2

Cc:	-

Contact person:	Mikael Wass

mikael dot wass at ericsson dot com

-

Send any reply LS to:	3GPP Liaisons Coordinator, mailto:3GPPLiaison@etsi.org

Attachments:	None

# 1	Overall description

CT1 thanks RAN2 for the LS on slice-based cell reselection and would like to respond to the questions asked as follows.

1. Can UE NAS provide to UE AS a list of slices (or slice group(s)), each with its corresponding priority for cell reselection evaluation in RRC_IDLE/RRC_INACTIVE?

Answer 1: CT1 assumes SA2 to agree a stage 2 solution on how a list of slices (or slice group(s)) with priorities is provided to UE NAS. Once such solution is agreed in SA2, CT1 can work on clarifying the related interaction between the NAS and AS layers.

2. Can the concept of Slice group and its signalling (Slice Group and its identifier) be supported using NAS signalling?

Answer 2: CT1 sees no issues to introduce support in NAS to convey information on Slice groups from the network to the UE. A solution would depend on requirements outside CT1 area of responsibility to configure Slice group information in the network, but once stage 2 requirements are available, CT1 can proceed with stage 3 NAS details.

# 2	Actions

To RAN2, SA2

ACTION: 	CT1 asks RAN2 and SA2 groups to take the information above into account for the further work on slice-based cell reselection.

# 3	Dates of next TSG CT WG1 meetings

CT1#133e	11th-19th November 2021	electronic meeting

CT1#133-bis-e	17th-21st January 2022	electronic meeting