3GPP TSG-CT WG1 Meeting #132-e	C1-215775

# E-meeting, 11-15 October 2021

Title:	LS on the De-registration for onboarding registered UE

Response to:

Work Item:	eNPN

Source:	CT1

To:	SA2

Cc:

Contact person:

Name:	Pengfei Zhang

E-mail Address:	zhangpengfei5g@vivo.com

Send any reply LS to:	3GPP Liaisons Coordinator, mailto:3GPPLiaison@etsi.org

Attachments:	None

# 1	Overall description

For the de-registration for onboarding registered UE, the statement in TS 23.501 is as following:

Based on ON-SNPN policies, the AMF may start an implementation specific timer once the UE has registered to the ON-SNPN for the purpose of onboarding. Expiry of this timer triggers the AMF to deregister the onboarding registered UE from the ON-SNPN.

However, it is not specified if AMF shall perform explicit de-registration or that the AMF can locally de-register the UE as like in the case of expiry of implicit de-registration timerr. Hence, CT1 would like to ask SA2 when the implementation specific timer expires,?

Q1:	does AMF, if the UE is in 5GMM_IDLE, page the UE to get into 5GMM_CONNECTED and then start a NW initiated de-registration to the UE or does the AMF does a local de-registration if UE is in 5GMM_IDLE?

Q2:	does AMF, if UE is in 5GMM_CONNECTED perform a NW initiated de-registration?

# 2	Actions

To SA2

ACTION: 	3GPP TSG CT WG1 kindly asks SA2 to answer above question.

# 3	Dates of next TSG CT WG1 meetings

CT1#133e	11th-19th November 2021	electronic meeting

CT1#134e	21st-25th February 2022	electronic meeting