3GPP TSG-CT WG1 Meeting #132-e	C1-215963

# E-meeting, 11-15 October 2021

Source:	Samsung

Title:	Eees_EASDiscovery_Unsubscribe operation for Eees_EASDiscovery API

Spec:	3GPP TS 24.558 v0.4.0

Agenda item:	17.2.16

Document for:	Agreement

1. Introduction

This pCR specifies Eees_EASDiscovery_Unsubscribe service operation.

2. Reason for Change

The Eees_EASDiscovery_Unsubscribe operation is defined in clause 8.5.4.6 of 3GPP TS 23.558. It is required to provide service operations details in stage#3.

3. Proposal

It is proposed to agree the following changes to 3GPP TS 24.558 v0.4.0.

* * * First Change * * * *

#### 5.3.2.6	Eees_EASDiscovery_Unsubscribe

##### 5.3.2.6.1	General

This service operation is used by the EEC to cancel an existing subscription for EAS discovery information.

##### 5.3.2.6.2	EEC unsubscribing to EAS discovery subscription from EES using Eees_EASDiscovery_Unsubscribe operation

To unsubscribe EAS discovery subscription from the EES, the EEC shall send an HTTP DELETE message to the EES, on the resource URI identifying the Individual EAS Discovery Subscription resource representation as specified in clause 6.3.2.3.3.2. Upon receiving the HTTP DELETE request, the EES:

a)	shall verify and check if the EEC is authorized to unsubscribe the Individual EAS Discovery Subscription resource;

b)	if the EEC is authorized to cancel the Individual EAS Discovery Subscription resource, then the EES shall unsubscribe the EAS discovery subscription identified by the subscriptionId;

Editor’s note: It is FFS how EEC can cancel the Individual EAS Discovery Subscription if EEC is not authorized.

c)	shall return the "204 Not Content" message to the EEC, indicating the successful removal of the subscription information.

* * * End of Change * * * *