3GPP TSG-CT WG1 Meeting #132-e	C1-215577

# E-meeting, 11-15 October 2021

Title:	LS on UE POLICY PROVISIONING REQUEST message

Response to:	LS S2-2106697/C1-215540 on UE POLICY PROVISIONING REQUEST message from SA2

Release:	Release 17

Work Item:	5G_ProSe, eV2XARC_Ph2, eV2XARC

Source:	CT1

To:	SA2

Cc:	CT3

Contact person:	Jiangyong(Scott)

jiangyong@catt.cn

Send any reply LS to:	3GPP Liaisons Coordinator, mailto:3GPPLiaison@etsi.org

Attachments:	None

# 1	Overall description

CT1 thanks SA2 for their LS on UE POLICY PROVISIONING REQUEST message in S2-2106697/C1-215540. CT1 would like to provide the following feedback on points.

There are completely competing opinions on SA2’s requirement on the LS:

Some companies think it is efficient that UE triggers the request for UE polices on demand. So the SA2’s solution, i.e. including UE POLICY PROVISIONING REQUEST in registration message, is a good optimization. And it can’t cause the PCF to send the multiple same UE polices.

So they advocate that it is needed to implement SA2’s solution in Stage 3.

Other companies have the opposite opinion:

- If needed, the PCF always includes the latest V2X and/or ProSe policy to UE based on the service specific information from UDR during the registration regardless of UE’s request for it. And PCF has the responsibility to update UE polices as soon as possible to keep the consistency of UE policies between the network and UE.

- UE has no the latest information of V2X and/or ProSe capability supported by network before registration, so including the request for certain V2X and/or ProSe policy is inefficient.

- It also can cause the PCF to send the multiple same UE policies to UE if both UE POLICY PROVISIONING REQUEST and UE STATE INDICATION are included in registration message

So they argue including the request for certain V2X and/or ProSe policy during registration is neither necessary nor efficient.

Therefore, CT1 cannot come into a conclusion on this issue at the moment and would like to ask the following question for clarification to SA2:

a) Whether the PCF shall include the latest V2X and/or ProSe policy to UE based on the service specific information from UDR during the registration regardless of UE’s request.

If the answer to a) is "YES", CT1 believes  the UE does not need to include "UE POLICY PROVISIONING REQUEST message" in the registration request when the UE needs to send"UE STATE INDICATION message" to the PCF during the registration procedure. Because the "UE STATE INDICATION message" can trigger the PCF to provide the UE policies based on the service specific information including the latest V2X and/or ProSe policy to the UE.

b) If the answer to a) is "NO", how PCF handles both UE STATE INDICATION message and UE POLICY PROVISIONING REQUEST message received at the same time of UE policy association establishment procedure.

If above aspects are clarified, CT1 can discuss to align with stage-2 requirement accordingly.

# 2	Actions

To SA2

ACTION: 	CT1 kindly asks SA2 to provide feedback.

# 3	Dates of next TSG CT WG1 meetings

CT1#133e	11th-19th November 2021	electronic meeting

CT1#133-bis	17th-21th January 2022	TBC