3GPP TSG-CT WG4 Meeting #99e	C4-204276

# E-meeting, 18th – 28th August 2020

| CR-Form-v12.0 |
| --- |
| CHANGE REQUEST |
|  | 29.515 | CR | 0014 | rev | 1 | Current version: | 16.1.0 |  |
| For HELP on using this form: comprehensive instructions can be found at http://www.3gpp.org/Change-Requests. |

| Proposed change affects: | UICC apps |  | ME |  | Radio Access Network |  | Core Network | x |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

| Title: | Correction of CodeWord Checking for UE Notification and Verification |
| --- | --- |
| Source to WG: | Qualcomm Incorporated |
| Source to TSG: | C4 |
| Work item code: | 5G_eLCS |  | Date: | 2020-08-18 |
| Category: | F |  | Release: | Rel-16 |
|  | Use one of the following categories: F (correction) A (mirror corresponding to a change in an earlier release) B (addition of feature), C (functional modification of feature) D (editorial modification) Detailed explanations of the above categories can be found in 3GPP TR 21.900. | Use one of the following releases: Rel-8 (Release 8) Rel-9 (Release 9) Rel-10 (Release 10) Rel-11 (Release 11) Rel-12 (Release 12) Rel-13 (Release 13) Rel-14 (Release 14) Rel-15 (Release 15) Rel-16 (Release 16) |
| Reason for change: | TS 23.273 (e.g. clause 6.1.2) describes how a codeword may be used to support UE privacy via UE notification and verification for a location request from an external client. The external client provides the codeword which may be conveyed to a VGMLC in an Ngmlc_Location_ProvideLocation Request service operation (as defined in TS 29.515) and is transfered (by the HGMLC or VGMLC) to the serving AMF in an Namf_Location_ProvidePositioningInfo Request service operation (as defined in TS 29.518). The codeword is then transferred to the UE in a supplementary services LocationNotification Invoke (defined in TS 24.080). The UE then verifies the codeword and may accept or reject the location request based on whether the external client included a correct codeword. The Codeword parameter is optional in both an Ngmlc_Location_ProvideLocation Request service operation and an Namf_Location_ProvidePositioningInfo Request service operation and thus its presence or absence could be treated as determing whether a serving AMF needs to transfer the codeword to a UE. However, both an Ngmlc_Location_ProvideLocation Request service operation and an Namf_Location_ProvidePositioningInfo Request service operation also include a UePrivacyRequirements parameter defined in TS 29.515 which includes a codeWordCheck parameter also defined in TS 29.515. The codeWordCheck parameter is defined in the OpenAPI YAML as a boolean type and indicates whether the codeword should be sent to the UE. The two parameters introduce several error cases and ambiguities – e.g. if the codeWordCheck parameter is included and set TRUE but the codeword parameter is not included or if the codeword parameter is included but the codeWordCheck parameter is not included. To resolve this, it is proposed to send a codeword to the UE only when the the Codeword parameter is present and when the codeWordCheck parameter is present and set to TRUE and to include a note stating this as part of the definition of the codeWordCheck parameter. |
| Summary of change: | Add a note to the definition of the codeWordCheck parameter to indicate that checking of the Codeword parameter (by the UE) applies only when the Codeword parameter is present and when the codeWordCheck parameter is present and set to TRUE. Some other small errors in the UePrivacyRequirements parameter are also corrected. |
| Consequences if not approved: | Inconsistency in AMF and GMLC implementation regarding support of the Codeword parameter leading to incorrect support including violation of UE privacy requirements or failure of a location request. |
| Clauses affected: | 6.1.5.2.2, 6.1.5.2.7 |
|  | Y | N |  |  |
| Other specs |  | X | Other core specifications | TS/TR ... CR ... |
| affected: |  | X | Test specifications | TS/TR ... CR ... |
| (show related CRs) |  | X | O&M Specifications | TS/TR ... CR ... |
| Other comments: |  |
| This CR's revision history: | Added applicability note to codeWord. Added impact on clause 6.1.5.2.2. |

******** FIRST CHANGE ********

##### 6.1.5.2.2	Type: InputData

Table 6.1.5.2.2-1: Definition of type InputData

| Attribute name | Data type | P | Cardinality | Description | Applicability |
| --- | --- | --- | --- | --- | --- |
| gpsi | Gpsi | O | 0..1 | Generic Public Subscription Identifier |  |
| supi | Supi | O | 0..1 | Subscription Permanent Identifier |  |
| externalClientType | ExternalClientType | M | 1 | External client type |  |
| locationQoS | LocationQoS | O | 0..1 | Requested location QoS |  |
| supportedGADShapes | array(SupportedGADShapes) | O | 1..N | Supported Geographical Area Description shapes |  |
| serviceIdentity | ServiceIdentity | O | 0..1 | Service identity |  |
| serviceCoverage | array(E164CountryCodeOfGeographicArea) | O | 1..N | A list of E.164 country codes for geographic areas (see ITU Recommendation E.164 [13]) where the LCS client is permitted to request and receive UE location information. |  |
| ldrType | LdrType | C | 0..1 | Location deferred request event type |  |
| periodicEventInfo | PeriodicEventInfo | C | 0..1 | Periodic event information of the location request for a target UE |  |
| areaEventInfo | AreaEventInfo | C | 0..1 | Area event information of the location request for a target UE |  |
| motionEventInfo | MotionEventInfo | C | 0..1 | Motion event information of the location request for a target UE |  |
| ldrReference | LdrReference | C | 0..1 | Notification correlation ID It shall be present in the request from NEF if it is allocated by NEF for the Deferred 5GC-MT-LR procedure. It shall be present in the request to VGMLC for the Deferred 5GC-MT-LR procedure. |  |
| hgmlcCallBackUri | Uri | O | 0..1 | Notification target address |  |
| externalClientIdentification | ExternalClientIdentification | O | 0..1 | External LCS client identification |  |
| afId | string | O | 0..1 | The identification of AF that initiated location request |  |
| uePrivacyRequirements | UePrivacyReqirements | O | 0..1 | UE privacy requirement |  |
| lcsServiceType | LcsServiceType | O | 0..1 | LCS service type |  |
| velocityRequested | VelocityRequested | O | 0..1 | Velocity of the target UE is requested |  |
| priority | LcsPriority | O | 0..1 | Priority of the location request |  |
| locationTypeRequested | LocationTypeRequested | O | 0..1 | Requested type of location, applicable to location immediate request |  |
| maximumAgeOfLocationEstimate | AgeOfLocationEstimate | O | 0..1 | Requested maximum age of the location estimate |  |
| amfId | AmfId | O | 0..1 | The identification of serving AMF |  |
| codeWord | CodeWord | O | 0..1 | Code word (NOTE Y) |  |
| NOTE Y: Checking of the Codeword in UE applies only when the Codeword parameter is present and when the codeWordCheck parameter (specified in clause 6.1.5.2.7) is present and set to TRUE. |

******** NEXT CHANGE ********

##### 6.1.5.2.7	Type: UePrivacyRequirements

Table 6.1.5.2.7-1: Definition of type UePrivacyRequirements

| Attribute name | Data type | P | Cardinality | Description | Applicability |
| --- | --- | --- | --- | --- | --- |
| lcsServiceAuthInfo | LcsServiceAuth | O | 0..1 | When present, this IE shall contain an indication of privacy related notification or verification for the target UE. The default value of this parameter if not presents is "LOCATION_ALLOWED_WITHOUT_NOTIFICATION". |  |
| codeWordCheck | boolean | O | 0..1 | When present, it shall indicate whether the Codeword parameter shall be checked in UE. (NOTE X) |  |
| NOTE X: Checking of the Codeword in UE applies only when the Codeword parameter (specified in clause 6.1.5.2.2) is present and when the codeWordCheck parameter is present and set to TRUE. |

******** END OF CHANGES ********