3GPP TSG-CT WG4 Meeting #99e	C4-204277

# E-meeting, 18th – 28th August 2020

| CR-Form-v12.0 |
| --- |
| CHANGE REQUEST |
|  | 29.515 | CR | 0015 | rev | 1 | Current version: | 16.1.0 |  |
| For HELP on using this form: comprehensive instructions can be found at http://www.3gpp.org/Change-Requests. |

| Proposed change affects: | UICC apps |  | ME |  | Radio Access Network |  | Core Network | x |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

| Title: | Correction of Notification or Verification only for UE Positioning |
| --- | --- |
| Source to WG: | Qualcomm Incorporated |
| Source to TSG: | C4 |
| Work item code: | 5G_eLCS |  | Date: | 2020-08-18 |
| Category: | F |  | Release: | Rel-16 |
|  | Use one of the following categories: F (correction) A (mirror corresponding to a change in an earlier release) B (addition of feature), C (functional modification of feature) D (editorial modification) Detailed explanations of the above categories can be found in 3GPP TR 21.900. | Use one of the following releases: Rel-8 (Release 8) Rel-9 (Release 9) Rel-10 (Release 10) Rel-11 (Release 11) Rel-12 (Release 12) Rel-13 (Release 13) Rel-14 (Release 14) Rel-15 (Release 15) Rel-16 (Release 16) |
| Reason for change: | With notification or verification only of positioning, a UE is either notified of location or notified and asked to verify the location by the serving AMF, but a location of the UE is not obtained. Instead, the serving AMF confirms to a HGMLC that the notification has occurred and, if verification was also performed, provides an indication of whether the location was allowed by the UE or disallowed. This feature can be used when UE location privacy preferences indicate privacy dependence on the current UE location. In that case, a current location of the UE is first obtained without any notification to or verification by the UE. The HGMLC then determines, based on the current UE location, whether the location is (a) allowed, (b) not allowed, or (c) requires notification to and/or verification by the UE. For case (c), the HGMLC can instigate a notification only or notification plus verification only request to the serving AMF via a VGMLC and waits for a response before deciding whether the current UE location can be sent to an external client or AF. The indication of case (c) by an HGMLC to a VGMLC can be conveyed in two separate parameters included in an Ngmlc_Location_ProvideLocation Request service operation. One of these parameters is the LocationTypeRequested parameter defined in TS 29.515 which is an ENUMERATION type with the following values. "CURRENT_LOCATION" "CURRENT_OR_LAST_KNOWN_LOCATION" "INITIAL_LOCATION" "NOTIFICATION_VERIFICATION_ONLY" The other parameter is the LcsServiceAuth parameter defined in TS 29.571 which is also an ENUMERATION type with the following values. "LOCATION_ALLOWED_WITH_NOTIFICATION" "LOCATION_ALLOWED_WITHOUT_NOTIFICATION" "LOCATION_ALLOWED_WITHOUT_RESPONSE" "LOCATION_RESTRICTED_WITHOUT_RESPONSE" "NOTIFICATION_ONLY" "NOTIFICATION_AND_VERIFICATION_ONLY" These parameters would conflict when one parameter indicates notification or verification without location (case (c) above) while the other parameter indicates that a UE location is needed. One way to resolve this inconsistency would be to remove the 2 parameter values highlighted above and treat the the LcsServiceAuth parameter as controlling the notification/verification aspect and the LocationType parameter as controlling whether the serving AMF obtains a location of the UE. Something like this was attempted at CT4-98e in C4-203287 for TS 29.518 where a similar conflict arose regarding the LocationType parameter in TS 29.518 but due to one error case which still remained in the CR and a preference (by some companies) not to remove the 2 highlighted parameter values, it was not agreed. Another resolution might be to remove the other parameter value highlighted above. However, this would still leave some inconsistency when the LocationTypeRequested indicated that a location is needed (e.g. "CURRENT_LOCATION", "CURRENT_OR_LAST_KNOWN_LOCATION") while the LcsServiceAuth parameter indicated that location is not needed. A third resolution would be to leave the current parameter values above and add a note to the definitions of LocationTypeRequested in TS 29.515 and LcsServiceAuth in TS 29.571 indicating that when a highlighted value for one of these parameters is included a highlighted value for the other parameter must also be included. This does not remove the possibility of inconsistency but it does clarify which combinations of values are allowed and which combinations are not allowed, which would allow implementations to avoid (at a sender) or recognize (at a receiver) the inconsistent parameter values. This CR supports the third resolution above. |
| Summary of change: | Add a note to the definition of the InputData to indicate that when the “NOTIFICATION_VERIFICATION_ONLY" value is used, then the LcsServiceAuth parameter defined in 3GPP TS 29.571, if present, shall be set to either NOTIFICATION_ONLY" or "NOTIFICATION_AND_VERIFICATION_ONLY". |
| Consequences if not approved: | HGMLC and VGMLC implementations may treat inconsistent values for the LocationTypeRequested and LcsServiceAuth parameters in different ways (e.g. may detect an error or may ignore one parameter value and react only to the other parameter value). This could lead to erroneous support for UE notification and verification and/or failure of a location request. |
| Clauses affected: | 6.1.5.2.2 |
|  | Y | N |  |  |
| Other specs |  | X | Other core specifications | TS/TR ... CR ... |
| affected: |  | X | Test specifications | TS/TR ... CR ... |
| (show related CRs) |  | X | O&M Specifications | TS/TR ... CR ... |
| Other comments: | This CR does not require version update on OpenAPI file |
| This CR's revision history: | Moved the note to InputData. Updated cover sheet other specs effected and other comments. |

******** FIRST CHANGE ********

##### 6.1.5.2.2	Type: InputData

Table 6.1.5.2.2-1: Definition of type InputData

| Attribute name | Data type | P | Cardinality | Description | Applicability |
| --- | --- | --- | --- | --- | --- |
| gpsi | Gpsi | O | 0..1 | Generic Public Subscription Identifier |  |
| supi | Supi | O | 0..1 | Subscription Permanent Identifier |  |
| externalClientType | ExternalClientType | M | 1 | External client type |  |
| locationQoS | LocationQoS | O | 0..1 | Requested location QoS |  |
| supportedGADShapes | array(SupportedGADShapes) | O | 1..N | Supported Geographical Area Description shapes |  |
| serviceIdentity | ServiceIdentity | O | 0..1 | Service identity |  |
| serviceCoverage | array(E164CountryCodeOfGeographicArea) | O | 1..N | A list of E.164 country codes for geographic areas (see ITU Recommendation E.164 [13]) where the LCS client is permitted to request and receive UE location information. |  |
| ldrType | LdrType | C | 0..1 | Location deferred request event type |  |
| periodicEventInfo | PeriodicEventInfo | C | 0..1 | Periodic event information of the location request for a target UE |  |
| areaEventInfo | AreaEventInfo | C | 0..1 | Area event information of the location request for a target UE |  |
| motionEventInfo | MotionEventInfo | C | 0..1 | Motion event information of the location request for a target UE |  |
| ldrReference | LdrReference | C | 0..1 | Notification correlation ID It shall be present in the request from NEF if it is allocated by NEF for the Deferred 5GC-MT-LR procedure. It shall be present in the request to VGMLC for the Deferred 5GC-MT-LR procedure. |  |
| hgmlcCallBackUri | Uri | O | 0..1 | Notification target address |  |
| externalClientIdentification | ExternalClientIdentification | O | 0..1 | External LCS client identification |  |
| afId | string | O | 0..1 | The identification of AF that initiated location request |  |
| uePrivacyRequirements | UePrivacyReqirements | O | 0..1 | UE privacy requirement |  |
| lcsServiceType | LcsServiceType | O | 0..1 | LCS service type |  |
| velocityRequested | VelocityRequested | O | 0..1 | Velocity of the target UE is requested |  |
| priority | LcsPriority | O | 0..1 | Priority of the location request |  |
| locationTypeRequested | LocationTypeRequested | O | 0..1 | Requested type of location, applicable to location immediate request (NOTEX) |  |
| maximumAgeOfLocationEstimate | AgeOfLocationEstimate | O | 0..1 | Requested maximum age of the location estimate |  |
| amfId | AmfId | O | 0..1 | The identification of serving AMF |  |
| codeWord | CodeWord | O | 0..1 | Code word |  |
| NOTE X: If the LocationTypeRequested parameter is set to "NOTIFICATION_VERIFICATION_ONLY", then the LcsServiceAuth parameter defined in 3GPP TS 29.571 [11], if present, shall be set to either “NOTIFICATION_ONLY" or "NOTIFICATION_AND_VERIFICATION_ONLY". |

******** END OF CHANGES ********