## Slide 1: RAN4-led topics in Rel-19: RRM & Demodulation
RP-233460
3GPP TSG RAN Meeting #102
Edinburgh, UK, 11th – 15th December, 2023
Agenda Item 9.1.4.3
Source: Nokia, Nokia Shanghai Bell

## Slide 2
Overview
RRM
Priority topics for RRM:
  Multi-Rx UEs
    Enabling LTM
    Supporting unified TCI framework
    Enabling simultaneous L3 measurements
  Further enhanced Early Measurement Reporting (EMR)
Observations on other RRM topics
Demodulation
Priority topics for Demod:
  Channel model with spatial component for realistic MIMO and MU-MIMO requirements
  Realistic Test Equipment EVM assumptions for improved testable MCS ranges and requirement accuracy
  Multi-RX demod requirements with joint processing
  Application layer throughput (ATP) requirements with outer loop link adaptation (OLLA)
Overall, the RAN4 RRM/Demod package should be limited to a small number of commercially relevant items

## Slide 3
Multi-Rx UEs: Enabling LTM
Background
Multi-Rx operation will enable future success of FR2 LTM. Especially for LTM, Multi-Rx can help link optimization mobility (LTM) performance.
Motivation
Rel-18 LTM solution does not support simultaneous neighbor cell L1 measurements and serving cell data reception.
UEs supporting multi-Rx can benefit from performing simultaneous L1 measurements on neighboring cell and data reception on serving cell.
  Proposals
  Enable simultaneous intra-frequency L1 measurements on LTM candidate cell and serving cell data reception without scheduling restrictions on the data reception.

## Slide 4
Background:
  RAN4 defined TCI state switching requirements for Multi-Rx using Rel-16 framework.
Motivation:
  RAN4 has defined unified TCI state switching requirements while not accounting Multi-Rx capable UE.
Proposal:
  Update unified TCI state framework to support Multi-Rx with simultaneous reception.
Multi-Rx UEs: supporting unified TCI framework

## Slide 5
Background:
  In Rel-18 only L1 scheduling restriction were improved while L3 scheduling restriction are postponed.
Motivation:
  Simultaneous measurements from more than one QCL type-D source on UE side may enable improved RRM requirements leading TP increase.
Proposal:
  Simultaneous data reception while performing L3 measurements using other Rx chain.
  Reduced L3 measurement delays by assuming more than single Rx for performing simultaneous L3 measurements.
Multi-Rx UEs: Enabling simultaneous L3 measurements

## Slide 6
Further enhanced Early Measurement Reporting (EMR)
Background:
RAN4 has been working on enhancing the RRM delay requirements. For Early Measurement Reporting, RRM delay requirements may be further enhanced on top of the Rel-18 enhancements. Rel-18 solution currently has no configuration or reporting (e.g., for UEs not supporting Rel-16 EMR).
Motivation:
The UE measurement accuracy and report delay requirement can benefit from further enhancements – building on the Rel-18 work.
The faster an SCell can be configured and activated the higher user TP and SCell usage can be obtained
Proposal:
  Based on Rel-18 enhanced measurement solution, define measurement accuracy and delay requirements for a selected carrier(s) for early reporting for fast SCell/PSCell configuration and activation.
  Informing network which selected one or more carriers have been and are being measured.
  Define needs for signaling support for configuration and reporting. Enable UE to report as soon as measurement results are ready (RAN2 impact).

## Slide 7
Observations on other RRM topics
Measurement Gaps
  The measurement gap framework has become excessively complex, with the result that many of the existing features are never likely to be deployed commercially.
  Further measurement gap related features are therefore not likely to be useful in practice.

## Slide 8
Channel model for realistic MIMO requirements (1/2)
1. Introduce a spatial component to the MIMO fading channel model
Motivation: The commonly used TDL-low MIMO fading channel model does not have a spatial component.
  Hence, MIMO SDM/precoding gains are not observable in performance requirements, due to lack of rank deficiency in the channel. All layers in SU-MIMO appear to have the same performance under these artificial conditions.
  Note that earlier discussions on use of CDL in Rel-15 were not completed due to lack of time, not lack of need. It is important now to establish a framework for testing in a spatially-realistic channel environment in readiness for 6G.
  2. Introduce CSI requirements for precoded MU-MIMO
    Motivation: No CSI requirements exist currently for precoded MU-MIMO with co-scheduled other users, as
      (a) Interference mitigation via PMI choice/reporting is ineffective in non-spatial channel models, and
      (b) The discussions about interference model implementation in TEs ran out of time in NR_eMIMO and NR_feMIMO.
    Requirements create visibility for improved UE PMI selection algorithm performance in MU-MIMO and corroborate investment in MU-MIMO deployments.

## Slide 9
Channel model for realistic MIMO requirements (2/2)
Objective
Add a channel spatial component to the channel model for MIMO and MU-MIMO requirements, e.g., by using the CDL model.
  Important for 8Rx/Tx systems with 2-codewords, as well as, 1-codeword cases where the precoding or precoding/receiver-interaction impact on performance is important.
  Important for CSI requirements on reporting precoders in MU-MIMO, which impact MU interference.
Testability aspects
CDL model can be implemented in the channel simulator of the test setup (see RAN4 BS setup figure). Major TE vendors offer CDL models in their vector signal generators and integrated/separate fading channel simulators, some explicitly based on [R4-1910399].
  In 38.901/38.827, CDL has been updated and maintained regularly by some contributors [e.g., R4-1910399]. Bugs and causes for unaligned performance were addressed [e.g., R4-1913676, R4-1904197]. Correlation matrices to model antenna configurations have been introduced.
TE vendors have highlighted CDL as the “forward compatible choice as it enables MU-MIMO modelling” [R4-1813242, R4-1811316], and TDL as “only appropriate for non-MIMO evaluations”.
Topics with questions arising from non-spatial MIMO channel models
8Rx, 2CW, 4Tx, 8Tx, MU MIMO setups/MU MIMO codebooks (NR_[f]eMIMO), coverage enhancement (also Rel-19), AIML, etc.

## Slide 10
Test Equipment (TE) TxEVM Assumption for Demod (1/2)
Background: What is the TE TxEVM assumption and what is it used for in legacy?
What is: Alignment and impaired simulation results have been provided with a TE TxEVM impairment of (e.g.) 6% up to 64QAM, 3% of 256QAM, and 2.5% for 1024QAM.
Usage 1: The max MCS and SNR test range limit was decided by not going to SNR values that have more than 1dB compression from TE TxEVM consideration.
Usage 2: The TE TxEVM give a DUT test/requirement relaxation at the upper MCS/SNR limit.
Motivation/Issues
Using a TE with better TxEVM performance than the assumption, results in significant test relaxation.
The MCS range is unnecessarily limited in many scenarios by TE TxEVM assumptions that are to conservative in RAN4.
  In Rel-18, the NonCol WI ran into TE TxEVM limitation due to needed operating point at 25dB for 256QAM.
The Demod testing is usually limited to <20dB baseband SNR due to TE TxEVM assumptions, which prohibits requirements in common BB SNR regimes of >20dB.
The discussion of TxEVM here only applies to TEs, not UE/gNB; and is limited to Demod, with its power levels and control over resource allocation, i.e., power budget.

## Slide 11
Test Equipment (TE) TxEVM Assumption for Demod (2/2)
Scenarios that are unnecessarily limited by legacy TE TxEVM assumptions
All FR1 conducted requirements.
  In FR1 conducted, the TE Tx power budget is not a limiting factor. The test range is only limited by the TE TxEVM assumption.
All FR2 OTA requirements, where Tx power budget is relaxed.
  In FR2 OTA, the testable range is often rather limited by power budget than TxEVM, but budget depends on FDRA.
  In AWGN channels this does not apply, as the fading channel margin in power budget is freed up.
  In requirements where the N_OC level is reduced (aka AWGN_offset).
All BS demod requirements,
  AWGN_offset can already be reduced by up to 15dB if testing requires it, so TxEVM limits can be improved.
Mitigatable Concerns
TE TxEVM depends on true resource allocation (esp. in CA)
  => Formula/resource allocation distinction to set meaningful TE TxEVM assumptions.
TE TxEVN depends on power levels
  Allow N_OC reduction in UE demod for testability reasons
The TE TxEVM assumptions are different between TEs for testing gNB/UE DUTs (different hardware and test setups).
  => Split any agreements in BS/UE DMD parts.
Objectives
Decide on realistic TE TxEVM assumptions in Demod to determine MCS/SNR test range.
  Includes TxEVM value and applicability in terms of modulation order, resource allocation, power, etc.
Decide whether to apply TE TxEVM in RAN4 impaired results derivation, or whether to leave TE measurement uncertainty/relaxation up to RAN5.

## Slide 12
Other potential UE Demodulation topics:
Multi-RX demod requirements with joint processing
Motivation: In Rel.18, RAN4 decided not to define requirements for UE joint processing. Consensus was to come back in later releases.
  Only requirements for 1 layer per TRP defined for sDCI SDM and mDCI fully overlapping. 2 layers per TRP only defined in the non-overlapping case.
Simulations showed that without joint processing in the fully-overlapping cases (2 layers / TRP), the cross talk between the TRPs and UE panels must be very low to achieve acceptable demodulation performance. This heavily limits the useful scenarios for MultiRx.
  In RAN4#108bis/109, companies provided simulation results for this configuration. Significant gain for, but not limited to, non-negligible cross talk scenarios were observed, when compared to separate processing.
The WID objective was to define requirements for up to 4-layer MIMO.
  We do not see this objective completed, as requirements are only defined with 2-layer on each TRP with FDM (i.e., non-overlapping), which does not qualify as 4-layer MIMO SDM.
Objective: Add requirements for 4-layer SDM/fully-overlapping MIMO at non-negligible inter-panel crosstalk. This will require 2 layers per TRP and UEs capable of joint processing across all 4 layers.
Application layer throughput (ATP) requirements with outer loop link adaptation (OLLA)
Motivation: In current ATP requirements the DUTs are seen to not adhere to the 10% BLER target in the CQI reporting. Hence the throughput shown in ATP is not representative of real deployments, where OLLA forces the BLER to 10%.
Objective: Introduce ATP requirements including OLLA, to better reflect performance in real deployments.

## Slide 13
Summary
RRM priority topics:
  Multi-Rx UEs
    Enabling LTM
    Supporting unified TCI framework
    Enabling simultaneous L3 measurements
  Further enhanced Early Measurement Reporting (EMR)
Demodulation priority topics:
  Channel model with spatial component for realistic MIMO and MU-MIMO requirements
  Realistic Test Equipment EVM assumptions for improved testable MCS ranges and requirement accuracy
  Multi-RX demod requirements with joint processing
  Application layer throughput (ATP) requirements with outer loop link adaptation (OLLA)
Overall, the RAN4 RRM/Demod package should be limited to a small number of commercially relevant items