## Slide 1
3GPP RAN#102 RP-233676 Edinburgh, UK December 11th – 15th, 2023
Considerations on Ambient IoT
EURECOM
Agenda Item: 9.1.1.4

## Slide 2: Background
The Rel-18 report on Ambient IoT TR 38.848 (V18.0.0) recommends the following to RAN:
RAN is recommended to down-select further starting from
  Deployment scenario 1 with Topology 1
  Deployment scenario 2 with Topology 1
  Deployment scenario 2 with Topology 2
  Deployment scenario 4 with Topology 1
  Deployment scenario 4 with Topology 3
FR1 licensed spectrum is recommended
  Note: selection or prioritization between FDD and FDD/TDD is to be decided
RAN is recommended to down-select to one or more of:
  Spectrum in-band to NR, in guard-band to LTE/NR, and in standalone band(s)

## Slide 3: Deployment Scenarios and Topology
“Simple” topologies 1 and 2 require the BS or the intermediate node to simultaneously generate a carrier wave (CW) for backscattering and to receive the back-scattered signal (Devices A&B)
This will require some HW modifications, e.g. isolated TX and RX antennas to recover the faint back-scattered signal from the strong CW
Technologies to achieve that exist (e.g. in RFID Readers) and are easier to implement than topologies requiring complex backhaul procedures (Topology 3 & 4)
Proposal: Focus on Topologies 1 & 2 and associated deployment scenarios

## Slide 4: Spectrum
Devices A and B require back-scattering transmission for UL communication
Back-scattering requires a time-continuous carrier wave
Thus, TDD is not able to support back-scattering without the device knowing the exact UL/DL pattern
In addition, device A needs to extract power from the DL transmission to operate its circuitry and decode the DL data
Without continuous DL transmission, device A cannot operate
Low carrier frequencies can achieve better coverage (especially important for devices A & B)
Unlicensed operation requires additional procedures (LBT) and can be considered in the future
Proposal: Focus on sub-GHz spectrum and licensed FDD (in-band, guard-band or standalone bands)

## Slide 5: Three Very Different Device Types…
Property | Device A (passive) | Device B (semi-passive) | Device C (active)
Complexity | Ultra-low | Low | Low/Medium
Energy storage | None | E1 | E2 (E2>E1)
Reception | Low-complexity Energy from incoming signal required for powering circuitry | Increased receiver sensitivity Independent power from ambient sources | Full low-complexity receiver Independent power from ambient sources
Independent Tx | No (back-scattering) | No (back-scattering) | Yes (but limited TX power)
Power consumption | <[1-10] | Hundreds of | <[1-10]
Link Budget and Range (see next slide) | DL-limited ~5-10m | Balanced link possible ~100m | UL-limited ~depends on tx power
Property | Device A (passive) | Device B (semi-passive) | Device C (active)
Complexity | Ultra-low | Low | Low/Medium
Energy storage | None | E1 | E2 (E2>E1)
Reception | Low-complexity Energy from incoming signal required for powering circuitry | Increased receiver sensitivity Independent power from ambient sources | Full low-complexity receiver Independent power from ambient sources
Independent Tx | No (back-scattering) | No (back-scattering) | Yes (but limited TX power)
Power consumption |  |  | 
Link Budget and Range (see next slide) | DL-limited ~5-10m | Balanced link possible ~100m | UL-limited ~depends on tx power
Different characteristics require specific physical layer design for each device type
Study needs to evaluate if and how the different devices can co-exist

## Slide 6: Example Link Budget
Free Space Pathloss @ 700MHz, PL (dB) = 29.35 + 20log(d)
Near Field @ 700MHz, until 2*lambda ~ 0.86m  28dB
Device A (Passive)
~10-30 μW IC power consumption to read tag
~30% rectifier efficiency  100 μW = -10dB at tag
-63dBm at reader
 Forward-link (DL) limited
Device B (Semi-Passive)
Rx power only large enough to decode data
Rx sensitivity ~ -30 to -40 dBm
Range of ~100m, high quality reader required
Adding LNA at tag requires even more RX sensitivity at reader
Balanced link possible but usually UL-limited
Device C (Active)
Rx sensitivity of (cheap) radio ~90dBm
Able to read tag from ~85km ! LOS conditions
Limited by TX power of tag, e.g. 10dBm (10mW)
 Unbalanced link (read the tag but not hear it)
Thermal Noise Floor ~ -110dBm for 180 kHz BW (1 PRB @ 15kHz) and receiver noise figure of 10dB
40
30
20
10
0
-10
-20
-30
-40
-50
-60
-70
-80
-90
-100
-110
-120
1
2
4
8
16
32
8.65 dBm
TX power
38 dBm
8.56 m
Required IC Power = -10 dBm
Backscatter Efficiency ~ 30% => 10log(1/3)=-4.77~5dB
RX power
-63 dBm
64
128
256
152 m
RX power
-113 dBm
10k
100k
85 km
Distance from Reader [m]
Power [dBm]
RX power
-118 dBm
5 dB
Directional antennas can improve link budget

## Slide 7: Proposals
Study UL/DL PHY design for all three Ambient IoT device types A,B,C
  DL (A): Received signal needs to power receiver circuitry
  UL (A/B/(C)): Back-scattering transmission design
  UL (C): UL waveform enabling power-efficient transmitter design
  DL (B/C): For in-band operation, WUS design can be starting point  Different device types require different waveforms/coding in UL and DL
  If prioritization among device types required  focus on A & B
Study PHY procedures
  Multiple access schemes (TX/RX of multiple devices of different type)
  Co-existence of all three device types (unified design to support all three device types)
  Potential measurements performed by devices
  Include energy harvesting in the evaluation methodology (communication uncertainty, does device have enough energy to receive/transmit)
Given amount of novelty in the air interface  SI only in Rel-19