## Slide 1: Way Forward on Fragmented Carriers in Rel-19
RP-240498
3GPP TSG RAN Meeting #103
Maastricht, The Netherlands, 18th – 21st March, 2024
Agenda Item 9.1.4.1
Source: TELUS, Bell Mobility, Nokia, Nokia Shanghai Bell, Telstra, T-Mobile USA, US Cellular, Spark NZ Ltd, Southern Linc, AT&T

## Slide 2: Motivation
Today, fragmented carriers in the same band consume multiple Rx chains, thus limiting the Carrier Aggregation (CA) capabilities
The maximum number of component carriers (CCs) in a CA combo is limited by the number and capabilities of the analog Rx chains in the UEs
This restriction exists only in the RF domain as some chipset vendors have already demonstrated that fragmented blocks require the same number of baseband processing units as single non-fragmented blocks
This limitation reduces customer experience by preventing us from fully utilizing our fragmented spectrum holdings in a single CA combo
A multi-company proposal was submitted to RAN#102[1] and RAN4#110[2] indicating this is a solution that would have global impact.
Observation 1: Fragmented carriers in the same band consume multiple Rx chains, thus limiting the CA capabilities
Observation 2: This restriction exists only in the RF domain as some chipset vendors have already demonstrated that fragmented blocks require the same number of baseband processing units as single non-fragmented blocks
Proposal: Study the use of fewer Rx chains than carrier fragments in a band
[1] RP-233374, “Fragmented carriers in the DL”, TELUS, Bell Mobility, Telstra, Nokia, Nokia Shanghai Bell, AT&T, US Cellular
[2] R4-2402309: “Study on effective utilization of fragmented FR1 carriers in the DL”, TELUS, Bell Mobility, Telstra, Nokia, Nokia Shanghai Bell, AT&T, US Cellular

## Slide 3: Scope
Study Item to identify a solution for minimizing the number of UE Rx chains needed for intra-band non-contiguous CA
Objective:
  Study methods by which a UE can dynamically switch the number of Rx chains (one or two) needed for a single DL band of ≤ 100 MHz within a CA combination, considering
    ACLR implications
    The near-far problem
RAN4 led item with minimal RAN2 impact and no RAN1 impact is foreseen
Timescale:
  Start Q3 2024
  Target completion Q2 2025
Note: When the study is complete, consider normative work to define core requirements using the identified solution