## Slide 1: Motivation for Tfi in 5GBC
Roland Beutler
EBU/SWR
Roland.beutler@swr.de
3GPP TSG RAN Meeting #106
Madrid, SPAIN, December 8-12, 2024
Agenda item: 10.1.1

## Slide 2
Background
In Rel-14 and Rel-16, RAN introduced a set of features under the umbrella of “LTE based 5G terrestrial broadcast” that, together with the corresponding enhancements in the core network, enable the deployment of a downlink-only dedicated broadcast network using 3GPP technologies.
The technology has been further evolved in Rel-17/18 by the introduction of 6/7/8MHz channel bandwidth and corresponding support of the broadcast UHF band, i.e. bands 107 and 108 which are in the range 470 – 698 MHz.
Since the initial standardization of LTE-based 5G Broadcast in Rel-16 [1] and subsequent enhancements to adapt to the broadcast UHF band [2,3], there has been significant ecosystem building and interest from broadcast network operators in this technology across the world.

## Slide 4
China
India
Malaysia
Indonesia
2022-2024: Tech demonstrations at IMC and BES events
2025: Proposal to run trial on national broadcast network
2024 : Initial meeting led by Ministry of Communications and Information (MCI) to define next steps towards trial in 2025
2024: Malaysian Technical Standards Forum released future broadcasting study report setting the stage for 5G Broadcast
2024: Malaysian Communication and Multimedia Commission (MCMC) organized 5G Broadcast test-bed facility session with BNOs, MNOs, device manufacturers in preparation of large scale trial in 2025
2023: Chengdu pilot project with live TV and public warning messages
2023: Global 5G Broadcast Summit Forum hosted by GATIS
2024: First 5G Broadcast over Astrum, L-Band GEO satellite
2025: Extending to phase 2 with additional sites and additional states
Driving test @ 60Km/h
Emergency notifications
5G Broadcast Trials - Asia

## Slide 5
USA
Mexico
Colombia
Brazil
2023: First experimental 5G Broadcast in Boston by XGN using existing infrastructure with no change in frequency, antenna, power output
2024-2025: XGN moved to Phase 2 and added three additional stations with experimental license to test SFN, emergency notifications, road sign update for emergency, first responder communication and channel bonding
2024: First demo with Moto Edge phones in Mexico City
2025: Larger trial covering center area of Mexico City
2020-2021: Delivery of TV and Radio with Rel-14 5G broadcast trial deployment in Santiago de Tolu
2024: First demonstration of 5G Broadcast combined with ISDB-T combined waveform
2023: Multi-angle 5G Broadcast demo during Rio Open
2024: Demo at Set Expo in collaboration between Claro, Globo, Motorola, Rohde & Schwarz and Qualcomm
5G Broadcast Trials - AMERICAS

## Slide 6
France
Germany
Italy
Czech Republic
UK
Austria
Spain
Greece
Estonia
2023: EU broadcasters signed MoU for 5G Broadcast for collaboration
2024: European 5G Broadcast Handset Taskforce released 5G Broadcast receiver profile for Europe
2018: First field trial in Aosta during Europe championship
2022: Demo on phones during Eurovision contest
2023: Test bed and field trials
2024-2025: Pre-commercial phase with live signal in 5 major cities
2024: large scale trial by TDF during Olympics using Xiaomi phones
2025: Additional tests for hybrid tests, interactivity, signal optimizations
2022: 5G VISTA project to study how 5G Broadcast could enable multi-angle HD streams with interactivity in stadiums
2028: TDF considering rolling out 5G Broadcast
2024: Live signal in 5 cities for advanced tests using Xiaomi phones and Qualcomm reference designs
2027: MediaBroadcast is planning to start commercial service
2022-2023: 5G Broadcast demonstrations at ISA and MWC shows with Cellnex Telecom
2025: 5G Broadcast trial in Valencia
2022: CRA ran 5G Broadcast tests in Prague
2024: CRA running new tests with SFN in two sites
2023: ORS used 5G Broadcast during MotoGP race
2022: Europe wide 5G broadcast trial delivering Eurovision in Italy, France, Germany, Austria
2023: Tested 5G Broadcast at Crevex 2023
2025: Further tests for alert functionality with integration to cell broadcast for news and critical updates
2021-2023: Live TV/Radio with 5G BC Rel-14/16 , with 3MHz in Athens
5G Broadcast Trials - EUROPE

## Slide 7
Motivation for new work item
While the above described trials of these technology have been ongoing, the following specification gap has been identified:
Unlike other state-of-the-art broadcast standards, LTE-based 5G broadcast does not support time-frequency interleaving (TFI), which severely impairs its performance in the presence of multipath and fading channels, up to several dBs.

## Slide 8
PROPOSAL
Specify Time-Frequency Interleaving for 5G broadcast, taking as baseline the design discussed in Rel-16 during RAN1#99 and captured in [4].
Chairman’s notes:

## Slide 9
SUPPORTing members FOR THE new work item
EBU, ABS, BNE, Cellnex, Eutelsat, ORS, TDF, SWR, XGN, Ateme, CUC, Dolby, IITB, one2many B.V.
Panasonic, Philips, Qualcomm, Rohde & Schwarz, UPV/EHU, Enensys, [SJTU]

## Slide 10
Time Interleaving proposal: 3GPP modem-friendly designs
Objective: Design that provides time diversity reusing LLR buffer memory at the receiver.
Basic Approach: Reuse of the 3GPP building block behind HARQ retransmissions and combining, which allows to spread the coded bits of a transport block (TB) across multiple non consecutive slots/subframes (similar as TBoMS across non-consecutive subframes).
Interleaved transmission of “redundancy versions” of transport blocks across subframes.

## Slide 11
Frequency interleaving
A codeblock may only span a small portion of the barrier bandwidth. Frequency interleaving (within an OFDM symbol) provides frequency diversity.
The proposed frequency interleaving is a row-column interleaving:
  1. The tones corresponding to an OFDM symbol are written row-wise.
  2. Pseudo random shifts are applied to the columns.
  3. Elements are read column wise.
For a detailed standards’ focused description on these aspects, see R1-1912692

## Slide 12
Performance gains with time and frequency interleaving
~4dB gain at 1% BLER
5.4dB gain at 0.1% BLER
More details of the simulation setup can be found in [6], and further results in [5].
5.4 dB

## Slide 13
KEY reasons for requesting TFI for 5G- BROADCaST
Reusing techniques already specified in 3GPP:
  The time-interleaving is performed by combining principles from NR PUSCH TBOMS and eMTC multi-TB scheduling with interleaving.
  The frequency-interleaving is a row-column interleaving, widely used in 3GPP.
Performance improvements beyond 5 dB;
Worldwide interest in this technology from different regions (US, Europe, China, India, Malaysia..)

## Slide 14
REFERENCE
[1] RP-191924 - WID for LTE-based 5G terrestrial broadcast
[2] RP-211144 - New bands and bandwidth allocation for 5G terrestrial broadcast - Part 1
[3] RP-211145 - New bands and bandwidth allocation for LTE based 5G terrestrial broadcast - Part 2
[4] R1-1913095 Information on Time Interleaving in State-of-the-Art Terrestrial Broadcast Systems, EBU/BBC/IRT/ABS/NHK
[5] Time and Frequency Interleaving for broadcast services in 3GPP Systems, 5G-MAG report – available online
[6] Ayan Sengupta, Javier Rodriguez Fernandez, Alberto Rico Alvarino, and Thomas Stockhammer, “5G Broadcast Receivers: Optimizing Performance under Implementation Constraints”, IBC 2023, Amsterdam.

## Slide 15
Annex - Row-Column Frequency Interleaving

## Slide 16
ANNEX - CYCLIC shifts for frequency interleaving