## Slide 1
gsoasatellite.com
info@gsoasatellite.com
@GSOA
@GSOA_SAT
@gsoa4satellite
Title: LS on 3GPP NTN Based Satellite Networks
Deployment Considerations
Contacts: Isabelle Mouro, Director General, GSOA (dg@gsoasatellite.com)
Munira Jaffar, Chair, GSOA Standards WG (Munira.Jaffar@EchoStar.com)
3GPP TSG-RAN # 107 RP-250032
Incheon Korea, March 12-5, 2025
To: TSG RAN#107, TSG SA#107

## Slide 2: Where We Are Today
Opportunity - NTN/TN integration is a reality, the success from 3GPP NTN marks a significant milestone, opening new avenues for growth and innovation
What about the deployment of NTN networks?
  The commercial deployment of Non-Terrestrial Networks (NTN) is progressing through multiple phases, with initial stages already underway.
  Early deployments are expected to enhance network services, including mobile connectivity for a range of applications such as voice, internet, and messaging.

## Slide 3: 3GPP NTN Based Satellite Network Deployment Considerations
Industry Interest from Satellite Network Operators on Various Deployment Considerations:
 | Narrowband connectivity to IoT devices (NTN-IoT in FR1) |  | Broadband connectivity to handheld devices (NTN-NR in FR1) | Broadband connectivity to non-handheld devices (VSAT) (NTN-NR in above 10 GHz Band) | 
Space Segment | Existing GSO | NGSO | NGSO | GSO | NGSO
Target Device | Smartphone, IoT devices | Smartphone, IoT devices | Smartphones and handheld devices | VSAT Mobile VSAT | VSAT Mobile VSAT
Release | Rel-17/Rel-18 | Rel-17, Rel-18, Rel-19 | Rel-17, Rel-18, Rel-19 | Rel-17, Rel-18, Rel-19 | Rel-17, Rel-18, Rel-19
Operators | EchoStar Viasat-Inmarsat Terrestar Solutions Skylo Ligado | EchoStar Sateliot OmniSpace Viasat-Inmarsat Iridium | EchoStar Viasat-Inmarsat OmniSpace SES Terrestar Solutions | Eutelsat Group Viasat-Inmarsat Intelsat SES Hispasat Ovzon | Eutelsat Group Viasat-Inmarsat Intelsat SES Hispasat
Best Estimates | 2023-2025 | 2024-2029 | 2026-2029 | 2026-2029 | 2026-2029

## Slide 4: GSOA Proposal on NTN in 3GPP Rel-20
Observation:
NTN standard is making encouraging impact to the SatCom and mobile industry
Satellite Direct-to-Device Connectivity Bringing Connectivity to Everyone, Everywhere, Anytime
GSOA Recommendation:
3GPP TSG RAN and SA to prioritize the definition of new features and capabilities for NTN and Sat5G_Arch in Rel-20 to enable improved performance, new use cases, and optimized interoperability with terrestrial networks.