## Slide 1
3GPP TSG RAN Meeting #108 RP-251207
Prague, Czech Republic, June 9-13, 2025
Agenda Item: 15.1.5
Source: vivo
Title: Scope of NR NTN phase 4 in 5G-A Rel-20
Document for: Discussion and Decision

## Slide 2
NR NTN phase 4 – GNSS resilient operation
Motivation & Background
  Both NR-NTN and IoT-NTN are designed to operate under the assumption that GNSS are available. However, it is possible that GNSS may not be available (in time and/or space) or may be less accurate
  Moreover, NTN is also an important deployment scenario for 6G. It is highly desirable to constructure a common radio design for TN and NTN in 6G. Thus, enabling the UE to access to NTN without GNSS is a key aspect of harmonized 6G Radio design for TN and NTN.
Proposal
  Study the potential mechanisms to support a UE to access to the NTN network when GNSS may not be available or may be less accurate
    Considering the limited TU, the study should focus on NR-NTN scenario.
    Nevertheless, the study should consider both NR-NTN and IoT-NTN scenarios, and aim to achieve a common design principle applicable to NR-NTN, IoT-NTN, and potentially 6G.
    Potential mechanisms may include, e.g., NTN-assisted positioning, close-loop time/frequency correction, UE Tx timing relaxation, etc.

## Slide 3
NR NTN phase 4 – E-UTRA TN to NR NTN handover
Motivation & Background
  In Rel-19, E-UTRA TN to NR NTN mobility WI only includes the inter-RAT cell (re)selection enhancements.
  Inter-RAT E-UTRA TN to NR NTN handover is important for ensuring seamless inter-RAT mobility.
Proposal
  Specify necessary enhancements to support E-UTRA TN to NR NTN handover in RRC connected mode
    Provide necessary satellite information in E-UTRA TN for NR NTN neighbor cell measurement.
    Define RRM requirements for E-UTRA TN to NR NTN handover.

## Slide 4
NR NTN phase 4 – WID Objectives
Objectives:
  Study the mechanism to support a UE to access to the NTN network when GNSS may not be available or may be less accurate (RAN1, RAN4, RAN2)
    Consider both NR-NTN and IoT-NTN scenarios
    Target for a common design principles that can be applied to NR-NTN, IoT-NTN, and potentially 6G
    Prioritize the NR-NTN scenario while the outcomes can be replicated on IoT-NTN scenario
  Specify necessary enhancements to support E-UTRA TN to NR NTN handover in RRC connected mode (RAN2, RAN4)
    Provide necessary satellite information in E-UTRA TN for NR NTN neighbor cell measurement.
    Define RRM requirements for E-UTRA TN to NR NTN handover.
TU: RAN1 (1 TU), RAN2 (0.5 TU), RAN4 (0.5 TU)