## Slide 1: Views on Rel-20 AI/ML for NG-RAN CMCC
3GPP TSG RAN Meeting#108 RP-251385
Prague, Czech Republic, June 9-13, 2025
Agenda: 15.3.1
Document for: Discussion

## Slide 2: Motivation
In RAN#107, RAN Chair’s Summary of 5G-Advanced in Rel-20 has the following endorsed WF on AI/ML for NG-RAN:
Based on the RAN Chair’s Summary, Rel-20 AI/ML for NG-RAN includes:
  1 or 2 new use cases out of QoE optimization, Network energy saving and Mobility (including Multiple-hop UE trajectory prediction)
  Rel-19 leftovers (if any) will be treated as well

## Slide 3: Study on New Use Cases
In Rel-19, some new use cases such as QoE optimization and multi-hop UE trajectory prediction were proposed, but not included due to limited time, we think these two cases should be studied with high priority due to higher commercial needs
Potential Objectives of Rel-20 SI:
  Study the new AI/ML based use cases, i.e., QoE optimization and Multi-hop UE trajectory prediction, with existing NG-RAN interfaces and architecture (including non-split architecture and split architecture):
    Study standardization impacts for the new use cases including: the data that may be needed by an AI model as input, data that may be produced by an AI model as output, and feedback data, which is interpretable for multi-vendor support
    Study standardization impacts on the network interface(s) in current NG-RAN architecture to convey the input/output/feedback data among network nodes
Proposal 1: The QoE optimization and multi-hop UE trajectory prediction are proposed to be studied in Rel-20

## Slide 4: Support of Rel-19 leftovers
Current progress of AI/ML for NR-DC:
  In Rel-19 WI, the mobility optimization mechanism was specified for NR-DC, including
    - Feedback collection (i.e., measured UE performance) from SN to MN
    - Signaling procedures for the configuration and reporting of UE performance collection
    - Conditions to start and stop the collection of UE performance at SN side
  However, there is no consensus achieved on the prediction information produced by AI model at MN side, which is the main benefit for AI/ML based Mobility Optimization
Therefore, AI/ML based Mobility Optimization for NR-DC is not yet complete, support of Rel-19 leftovers should take Mobility Optimization for NR-DC into account
Proposal 2: It’s proposed RAN to take Mobility Optimization for NR-DC as Rel-19 leftovers in Rel-20 WI

## Slide 5: Proposal on Rel-20 AI/ML for NG-RAN WI
  Specify data collection enhancements and signaling support within existing NG-RAN interfaces and architecture (including non-split architecture and split architecture) for new use cases, including:
    QoE Optimization
    Multi-hops UE trajectory across gNBs
  Support of the Leftovers in Rel-19 AI/ML for NG-RAN
    Mobility Optimization for NR-DC
Proposal 3: It’s proposed RAN to take the above as baseline to discuss potential objectives for Rel-20 WI

## Slide 6: Potential New Use Case - QoE Optimization
AI-based QoE performance guarantee during mobility: (focus on RVQoE)
  QoE prediction for resource allocation, e.g. whether more resources are needed to guarantee enough buffer and prepare in advance
  Maintain user experience during handover
QoE measurements collection for prediction validation
  Collect QoE related measurements/metrics after handover to evaluate AI/ML model
  Resource reallocation after handver
  Analyze whether more RVQoE metrics need to be introduced and collected for AI, if needed
RAN-visible QoE information reporting
Example: Signalling procedure for AI-based QoE Optimization

## Slide 7: Potential New Use Case - Multi-hop UE trajectory Prediction
UE trajectory prediction transmission
  UE Trajectory prediction (including prediction of multi-hops) transmission across gNBs, e.g. from one node to the next hop node in order
  UE trajectory prediction validity information, to avoid confusion caused by outdated prediction information
Measured UE trajectory collection
  Node/Cell level measured UE trajectory
  Measured UE Trajectory collection mechanism, e.g. from one node to the previous hop node in order
Multi-hop UE trajectory across gNBs
Example: Signalling procedure for multi-hop UE trajectory

## Slide 8: Thank you