## Slide 1: Motivation for improvements to CS/PS coordination in UTRAN Shared Networks
Ericsson RP-150306

## Slide 2: Background
The SA2 WI on Improvements to CS/PS coordination in UTRAN/GERAN Shared Networks investigated all mobility scenarios in order to identify issues with CS/PS coordination in the case of network-controlled mobility into UTRAN shared networks.
  i.e. issues where CS/PS coordination may fail resulting in the UE ending up registered to different operators in the CS and PS domains.
The investigation part of the SA2 work is documented in TR 23.704, together with a conclusion.
TS 23.251 (Network Sharing; Architecture and functional description) has already been enhanced with the result of the SA2 work, but no stage 3 work has been done so far.

## Slide 3: Proposed RAN Work Item
RAN aspects for improvements to CS/PS coordination in UTRAN Shared Network
  enhance UTRAN specifications according to the CS/PS coordination solutions specified in TS 23.251 to ensure that CS/PS coordination can be achieved for all mobility scenarios into UTRAN shared networks
Scope of proposed RAN work item
  Enhance the Iu interface with:
    Possibility for the SRNC to query the MSC(s)/ SGSN(s) whether the UE is served by any of the sharing operators.
    Possibility to transfer Old LAI/RAI, CS/PS-NRI and indication if UE is attaching in the Redirection Indication IE