## Slide 1: Motivation for new Study Item on NR Positioning
CATT
3GPP TSG RAN #75
Dubrovnik, Croatia, 6 - 9 Mar 2017
RP-170405

## Slide 2: Introduction
UE positioning has been a key feature in 3GPP due to the commercial applications and the US FCC E-911 requirements.
3GPP has developed the architecture, the interfaces, the protocols and the procedures, as well as various methods for supporting positioning operations for 3G/4G systems.
3GPP is now working on the new 5G network with New Radio(NR) Access Technology (RAT) with a new set of designs with advanced features
5G will post more stringent requirements on NR positioning than 3G/4G.
IoT and location based services are expected to be dominant services in 5G
It is critical to start exploring the challenges, requirements and solutions as early as possible in order to support the positioning applications for the first release of NR network.

## Slide 3: Key requirements of NR positioning
NR positioning technologies face much more stringent requirements than 3G/4G positioning
  Accuracy. In the order of a few meters or even sub-meters for high performance real-time applications.
  Reliability. High reliability for mission critical applications.
  Time latency. Short time to first fix (TTFF) for time critical applications, e.g., URLLC services.
  Coverage. Indoor and Outdoor in various deployment scenarios.
  Horizontal and vertical positioning. Both 2D and 3D locations.
  Scalability. Number of UEs in orders-of-magnitude increase from current 3G/4G network.
  Power Consumption. Extremely low power consumption for some applications, e.g., mMTC services.
It is essential to have simple and efficient NR positioning architecture for supporting above requirements.

## Slide 4: E-UTRAN UE Positioning Architecture
E-UTRAN UE positioning architecture:
  MME: handle location services requests and forward to E-SMLC
  E-SMLC: provide assistance data to UE to assist with UE-based and/or UE-assisted positioning , and/or provide position solution.
  eNodeB: control the cells for supporting of PRS-based TBS or other positioning approaches.
  UE: provide UE measurements for UE-based and/or UE-assisted positioning .
  SLP: responsible for positioning over the user plane.
  LMU: support uplink based position solutions
UE Positioning Architecture applicable to E-UTRAN
(TS 36.305)

## Slide 5: NR UE Positioning Architecture
It is essential to start the investigation on the NR positioning architecture to support the challenging 5G positioning requirements due to:
  unprecedented number of UEs to be supported.
  a wider variety of use cases, e.g.,
    highly accurate and reliable UE position information with very short latency, e.g., URLLC applications
    extremely low power consumptions , e.g., mMTC applications
  diverse deployment scenarios
    standalone and non-standalone
    licensed and unlicensed bands,
    dense-urban, urban, suburban, and rural areas.
  smooth integration with existing 3G/4G and other RAT positioning systems

## Slide 6: 5G System Architecture
5G system architecture is still in early study phase:
  NG RAN: Next Generation Radio Access Network
  LMF : Location Management Function
  AMF: Access and Mobility Management Function
  GMLC: Gateway Mobile Location Centre
  LRF: Location Retrieval Function.
  LMU: support uplink based position solutions
  UDM: Unified Data Management
Non-roaming reference architecture for Location Services
(TS 23.501 v0.2.0)

## Slide 7: Network interfaces for positioning operations
E-UTRAN network interfaces for supporting positioning operations
  LTE-Uu interface: connecting the UE to the eNode B over the air.
  S1-MME interface: between the eNode B and the MME.
  SLs interface: between the E-SMLC and the MME
  SLm interface: between the E-SMLC and an LMU for uplink positioning
5G network will re-define and develop new network entities and network interfaces for supporting 5G applications.
It needs further investigation on how to support the positioning operations with the new network entities and interfaces.

## Slide 8: Positioning Protocols
E-UTRAN positioning is supported by following C-plane protocols
  LTE Positioning Protocol (LPP): carry information between the UE and the E-SMLC
  LTE Positioning Protocol Annex (LPPa): carry information between the eNode B and the E-SMLC.
  Radio Resource Control (RRC): carry LPP messages and positioning measurements over the Uu interface.
  S1 Application Protocol: carry LPP/LPPa messages over the S1-MME interface.
  SLm Application Protocol: carry positioning messages between the E-SMLC and the LMU.
Protocols supporting NR positioning
  NR Positioning Protocols should be developed with consideration of LPP/LPPa protocols
    LPP/LPPa protocols were developed with the consideration of forward-compatibility with other RATs to avoid creating new positioning protocols
  NR will define the new RRC protocol with the objective of network functions virtualization (NFV) and network slicing. The transport for NR positioning messages and measurements should be supported with the new RRC protocol.
  Other application protocols responsible for message transportation between new network entries also need to be investigated.

## Slide 9: UE Positioning Procedures
Positioning procedures are defined as transactions of the protocols.
For E-UTRAN, 3GPP has defined the necessary positioning procedures (e.g., LPP/LPPa/SLmAP procedures) for supporting positioning applications.
New positioning procedures will need to be developed for supporting NR location applications based on the new 5G network architecture, interfaces, and protocols.

## Slide 10: Positioning Methods
UE positioning can be standalone (e.g., GNSS) or network-assisted (e.g., network-assisted GNSS, OTDOA, UTDOA, etc.)
3GPP has been focusing on the network-assisted positioning methods, although standalone methods are also supported.
Network-assisted positioning has two operating modes:
  UE-assisted
  UE-based
Positioning technologies based on 3GPP signals can be:
  Downlink positioning methods, where UE position is estimated based on measurements of downlink reference signals, e.g., OTDOA, PRS-based TBS,
  Uplink positioning methods, where UE position is estimated based on measurements of uplink reference signals, e.g., UTDOA, E-CID.
Other positioning technologies, which are not based on 3GPP signals, may also be supported
  Barometric pressure sensor positioning methods
  WLAN positioning methods
  Bluetooth positioning methods
  TBS positioning methods

## Slide 11: Proposals
Start a new NR positioning Study Item with the objectives of
  Investigate simple and efficient NR positioning architecture for location services, functional interfaces, protocol and procedures for supporting both RAT dependent and RAT independent positioning technologies [RAN2, RAN3, RAN1]
    Study the functional architectures and interface to integrate RAT independent positioning technologies
  Study NR dependent positioning technologies, such as OTDOA, UTDOA, ECID, that is coherent with NR mobile data communication framework. [RAN1, RAN2, RAN4]
    Define evaluation methodologies for the NR positioning technologies
  Identify 2D and 3D performance requirements of the NR positioning technologies for supporting location based applications and location assisted functionalities [RAN1, RAN4]