## Slide 1: 3GPP TSG RAN Meeting #75 Dubrovnik, Croatia, March 6 - 9, 2017 Agenda item: 10.1.1 Document for: Discussion
Motivation for further enhancement of NB-IoT for LTE
RP-170684

## Slide 2: Justification
In Rel-14, two work items, eMTC and NB-IoT, were approved to address the requirements of cellular internet of things.
However , the scope of WID was reduced during the WID discussion as a result of limited TU time available.
Some features were further delayed in WG discussion
As the actual network deployment started, it is important to ensure that IoT devices and IoT traffic can be handled efficiently in the networks ,and service requirements can be satisfied

## Slide 3: Objectives
Power consumption and latency reduction enhancement
Spectrum efficiency and coverage enhancement
Positioning enhancement

## Slide 4: Power consumption and latency reduction enhancement
Device power consumption is of paramount importance for NB-IoT success. Currently, feedback from field deployment and actual comparison with competing technologies shows room for improvement and calls for immediate attention.
Latency reduction is beneficial for many IoT services.

## Slide 5: Power consumption and latency reduction enhancement (1)
Status | Ave power consumption (mA) | Ave time % | Ave usage
Actual TX period | 400 | 17% | 43%
Non TX RRC connected period | 180 | 50% | 56%
IDLE period | 3 | 33% | 1%
For IoT applications, lots of the traffic is characterized by small packet data transmission. Improving access and transmission efficiency for small data transmission will lower UE power consumtpion.
Objective:
  Specify enhancement to improve UE power consumption and efficiency of small packet transmission [RAN1, RAN2]

## Slide 6: Power consumption and latency reduction enhancement (2)
SI latency enhancement [RAN1, RAN2]
  SI transmission enhancement via IoT specific SIB to reduced UE monitoring requirement and network access latency
Chart: Expected Latency reduction for some SIB Transmission
 | 2560 | 5120 | 9560 | 29440

## Slide 7: Power consumption and latency reduction enhancement (3)
  Study and specify enhancement for PRACH performance and capacity [RAN1, RAN2][NB-IoT only]

## Slide 8: Spectrum efficiency and coverage enhancement
With deployment of multiple PRBs , it is desirable for terminals to efficiently utilize available bandwidth .
  More bandwidth for increased data rate , for example , utilizing two PRBs at the same time to increase data rates will benefit some high data rate IoT applications deployed in the network.
Multiple HARQ processes can be used to further increase the data rates.

## Slide 9: Spectrum efficiency and coverage enhancement
  Paging enhancement [RAN1, RAN2]
    Paging transmission enhancement via common PO to reduce resource utilization
    Potential paging reduction
Pagingcycle | 128 | 256 | 256
PO reduction | 512 | 512 | 512

## Slide 10: Spectrum efficiency and coverage enhancement
  Signaling support for multi-carrier operation enhancement [RAN2, RAN4]
    Support of NB-IoT multi-carrier operation for standalone mode with either guard-band and/or in-band mode of operation
  Specify support of multiple HARQ process to further improve UE data throughput [RAN1,RAN2]

## Slide 11: Positioning support
UTDOA were studied in Rel-14.
Compare with OTDOA, UTDOA has the advantage of lowering UE complexity and UE power consumption in some deployment scenario
  In OTDOA, UE implementation of RSTD measurement increases UE complexity
  In OTDOA , UE measurement feedback increase UE power consumption , particularly for UE in extreme coverage scenario
However, UTDOA was finished due to concerns of potential interference of NPRACH for some scenario

## Slide 12: Example of UTDOA Configuration for feasible UTDOA deployment scenario

## Slide 13: UTDOA agreement in Rel-14
Rel-13 NPRACH preamble is the best candidate and can be used as a signal for NB-IoT UTDOA in some scenarios.
  Whether it is feasible in a given network deployment depends on issues including network coordination, interference handling, power control, in-band emissions, capacity impacts, etc.
Companies are encouraged to identify in RAN1#87 scenarios where it is and is not feasible

## Slide 14: UTDOA Objective in Rel-15
Based on Rel-14 study phase result, identify feasible deployment scenario and specify support for UTDOA based positioning
Candidate reference signal is based on Rel-14 NPRACH with necessary enhancement, considering multiple PRB deployment scenario
Evaluate the impact of interferences with positioning reference signal and identify feasible deployment scenario

## Slide 15: Thank you