## Slide 1: Motivation for new WID proposal on UE assisted performance enhancement
Apple
3GPP TSG RAN meeting#83
Shenzhen, China, March 18-21, 2019
RP-190259

## Slide 2: Background
Limitation of current NW scheduling and configuration
  For short-term scheduling
    Based on short term traffic statistics, e.g. flow control, buffer status, and UE radio quality, etc.
  For long-term scheduling/network resource allocation
    E.g. SCell activation/deactivation, UL In-sync/out-sync state change
    Long term traffic characteristics is beneficial for NW efficient long-term resource allocation. However, current NW has limited knowledge of long-term traffic pattern.

## Slide 3: Background
Compared to NW, UE has better knowledge of long-term traffic characteristics
  Limited NW knowledge of traffic pattern is via QoS/5QI parameters from CN
    Usually NW categorizes all applications using HTTP in non-GBR class.
  Accurate UE knowledge of the HTTP-type service, which includes several different traffic classes
    Background Traffic, Instant Messaging, Gaming, Interactive Content Pull and HTTP Video Streaming.

## Slide 4: Motivation
Modern smart phones nowadays have quite a lot of advanced information which could assist NW to further improve the AS-level scheduling and configuration
  The information includes the application specific traffic characteristics regarding application, traffic pattern and volume, etc.
With those information could improve the performance of both UE and NW
  More efficient RRC-state/CDRX/BWP/CA management and scheduling
  More efficient NW resource utilization
  Better UE power consumption
  Better user experience: e.g. lower latency

## Slide 5: Proposal
To setup an R16 WI with following objectives:
  Identify and specify mechanisms of scheduling optimization utilizing the application layer information
    Identify the limitation on current CDRX/BWP/CA/RRC-state operation due to traffic characteristics specific to applications, and potential enhancements
    Specify the mechanism for UE to suggest/feedback the AS configuration taking the application information into account
    Leading WG: RAN2

## Slide 6: Thanks!
3GPP TSG RAN meeting#83
Shenzhen, China, March 18-21, 2019
RP-190259