## Slide 1: Way Forward on NR Compression
CATT, CMCC, China Telecom, MediaTek Inc.
RP-190309
3GPP TSG RAN WG Meeting #83
Shenzhen, P.R.China, Mar. 18th -21st, 2019
Document for: Discussion
Agenda Item: 9.3.7

## Slide 2: Motivations for NR Compression
Motivation 1: Support in E-UTRA
  without UDC support in E-UTRA in 5GS, E-UTRA in NG-RAN is less radio efficient than E-UTRA in E-UTRAN
Motivation 2: Support with “Option 3” (ENDC)
  without UDC support in NR PDCP, E-UTRA in Option 3x is less radio efficient than E-UTRA in Option 3a.
Motivation 3: Mobility performance
  without a harmonized UDC support in E-UTRAN and NG-RAN, mobility performance can be impacted due to the necessity to perform an extra decompression/compression when going from E-UTRAN/NG-RAN to NG-RAN/E-UTRAN.
Motivation 4: Voice performance with NR (Options 3/2/4/7)
  UDC can improve the voice robustness for NR e.g. with Option 2.
  Without UDC Support in NR, voice performance with NR in Option 3x is worse than with Option 3a.
Motivation 5: harmonization
  Harmonization of UDC support between E-UTRA in EPS, E-UTRA in 5GS and NR ensures consistent performance across RATs and deployment scenarios.
Motivation 6: Low-hanging fruit
  The support of UDC in NR and in E-UTRA in 5GS is a low-hanging fruit that requires minimal additions to NR UP.
Motivation 7: relive the power constraint
  The power concern becomes more critical for NR deployment both for UE and network:
    New NR bands are mainly TDD, where DL and UL coverage disparity exists.
      HPUE can be useful tool, but the effectiveness is bounded by “allowed maximal duration”.
    Tx power is shared for NR and LTE for EN-DC deployment.
  Applying data compression onto UL data can relive the power constraint.

## Slide 3: Motivations for NR Compression
New motivation
  It has been identified in the study of UE capability signaling optimization SI, that compression is a feasible solution for CP signaling reduction.
  Due to compression function is not yet available at NR UP, the SI did not conclude to recommend compression into normative phase.
  However, uplink compression on CP signaling can greatly reduce the size of UE capability signaling.
    See following page for simulation results

## Slide 4: Some Simulation Result on UE Capability Compression
 | UE capability size (bytes) | Size reduction
Case 1 [3] | 3161 | 59%
Case 2 [2] | 1082 | 46%
Case 3 [4] | 300 | 30% - 50%
Table 1. UE capability size reduction by pure compression
 | UE capability size (bytes) | Size reduction
Case 1 [3] | 3161 | 98.8%
Case 2 [2] | 1082 | 98.3%
Table 2. UE capability size reduction by compression with dictionary
 | Dictionary size (bytes) | UE capability size (bytes) | Minimal size reduction | Average size reduction | Maximal size reduction
Case 1 [3] | 3161 | 3255 | 61.8% | 81.6% | 95.8%
Case 2 [2] | 1082 | 1114 | 46.6% | 77.8% | 95.4%
Table 3. Compression performance on UE capability whose content is slightly different from pre-defined dictionary
Note: Simulation results are from R2-1900479

## Slide 5: Status of previous discussion on NR UDC
The discussion and conclusion in RAN#79 on NR UDC:
  RAN chair: it seems NR voice works without it in REL-15, so it seems to be an optimization and can be brought up for REL-16.
The discussion and conclusion in RAN#80 on NR UDC:
  Unfortunately, the corresponding WID was not treated at all and was not part of the approved SI/WI Rel-16 package.
  Current plan is to finish it in TEI16 which will start in August meeting, 1TU for each meeting.
Proposal 1: Introduce UDC (DEFLATE) support in E-UTRA (5GS) and NR in Rel-16, using E-UTRAN UDC as a baseline.
Proposal 2: Use TEI16 for this work.

## Slide 6: Potential scope of NR compression WID
NR UDC :
  Adopt DEFLATE algorithm for 5GC-EUTRAN
  Adopt DEFLATE algorithm for 5GC-NR
  Support compression for
    Selective UP data
    CP signaling, at least for UE capability signaling
  Specify corresponding signalling and procedures