## Slide 1: Motivation for new WI on introduction of GSM, UTRA, E-UTRA and NR capability sets (CS(s)) to the MSR specifications
RP-190353
Ericsson, Vodafone, Orange, CKH IOD UK, CMCC, Telecom Italia, Huawei, HiSilicon, Deutsche Telekom

## Slide 2: Background
In rel-9&11, RAN4 developed the Multistandard Radio BS specification 37.104 for BS transmitting/receiving, multiple RATs (GSM, UTRA, E-UTRA and in later releases NB-IoT) from the same RF transceiver.
37.104 defines common requirements for all RATs. Test configurations that test RAT combinations are specified in TS 37.141.
In some regions (e.g. Europe), 37.104 is incorporated into regulation and is necessary for operating multiple RATs from the same RF
In the conformance spec 37.141, several so-called “capability sets” (CS) are defined. A capability set defines which combinations of RATs the BS supports.
During Release 15, RAN4 has developed a BS RF requirements specification for NR in 38.104, covering FR1 and FR2
To enable spectrum re-farming scenarios, NR has been incorporated into 37.104 so that transmission of NR+LTE from the same transmitter can be supported.
In rel-15, only capability sets including LTE, NR and NB-IoT were defined
This means that GSM and UTRA can be supported in different transmitters of a BS to NR, but cannot be supported together with NR on the same RF whilst being 3GPP compliant.

## Slide 3: Motivation
In some regions, GSM and UTRA are still operated and are likely to continue to be used even after partially re-farming certain bands
Re-farming scenarios mean that there are certain bands in which it would be desirable to re-farm towards NR, whilst still supporting GSM, UTRA and E-UTRA
It may be undesirable to transmit GSM and UTRA from separate base-station/transceiver to E-UTRA/NR within the same band
MSR specification with CS including GSM, UTRA, E-UTRA and NR would enable power sharing between different RATs in these scenarios

## Slide 4: Description of work - core
Certain requirements, in particular operating band unwanted emissions differ between GSM, UTRA and E-UTRA/NR
The current 37.104 specification applies in most cases masks for E-UTRA+NR operation that are not compatible with the GSM and UTRA emissions requirements
There is no need to develop new emissions requirements; what is needed is to decide which requirements should be applicable for the new capability sets and update the core specification in accordance with these decisions
The structure of the core specification for operating band unwanted emissions is becoming complex and an approach to structuring the updated specifications that does not further increase this complexity should be sought.
Some updates to the core requirement specification are likely to be needed

## Slide 5: Description of work - conformance
The conformance specification 37.141 contains a description of the capability sets
A capability set containing all RAT combinations would entail a large number of possible combinations. A discussion and conclusion is needed on which combinations are useful to support and how many new capability sets are needed.
There exists the risk of a large number of test combinations. A means of rationalizing the number of test configurations whilst still providing sufficient test coverage across all RATs is needed.
Some updates to the conformance test requirements to align to the core specification are likely to be needed