## Slide 1: Motivation for correction to aperiodic CSI-RS triggering with different numerology between PDCCH and CSI-RS
3GPP TSG RAN Meeting #83
Shenzhen, China, March 18th-21st, 2019
Agenda Item: 9.2.1
Source: Ericsson
Document for: Discussion, Decision
RP-190631

## Slide 2: Background
Cross-carrier scheduling with mixed numerologies
  At RAN plenary #81, cross-carrier scheduling with mixed numerologies was postponed to the Rel-16 WI on MR/DC (RP-182014)
“Cross-carrier scheduling with different numerologies is postponed to Rel-16. Already-agreed functionality for cross-carrier scheduling with different numerologies will not be removed from the Rel-15 specs, but will have a note added that the behaviour does not apply in this release.”
UL
PUSCH
DCI
Self-scheduling PUSCH (Supported in Rel-15)
Carrier X (µ1)
Cross-carrier scheduling PUSCH (not supported in Rel-15)
PUSCH
Carrier Y (µ2)
µ1≠µ2

## Slide 3: Background
DCI on Carrier X scheduling PUSCH on Carrier X with aperiodic CSI report for Carrier Y based on aperiodic CSI-RS
  Same numerologies between carriers X and Y: Supported in Rel-15
  Different numerologies between carriers X and Y: Currently not supported in Rel-15
In RAN1#92bis, this scenario was discussed. RAN plenary guideline, led to the following conclusion :
  “Triggering A-CSI reports whose measurement resources are with different numerology from that with PDCCH is not supported in Rel-15. “
Carrier Y (µ2)
UL
PUSCH
DCI
Carrier X (µ1)
µ1= µ2
A-CSI report
Carrier Y (µ2)
UL
PUSCH
DCI
Carrier X (µ1)
µ1≠µ2
A-CSI report
CSI-RS
UL
CSI-RS

## Slide 4: Triggering and Scheduling Clarifications
In this scenario, the DCI achieves the following
  Self-carrier scheduling: DCI on Carrier X schedules PUSCH on Carrier X to carry “A-CSI report”
  Triggering “A-CSI report”: Provides link to a CSI-RS configuration for measurements
    Occasion of CSI-RS is obtained from the configuration (DL BWP and Offset)
This scenario does not involve “cross-carrier scheduling”
Rel-15 supports the feature for the same SCS btw carriers.
UL
PUSCH
DCI
Self -scheduling PUSCH with A-CSI report
Carrier X (µ1)
Carrier Y (µ2)
µ1≠µ2
A-CSI report
CSI-RS resources for measurement obtained from configuration
CSI-RS

## Slide 5: Importance of CSI-RS triggerring by a carrier w different SCS
Crucial for Inter-band CA between low-band and high-band:
Beam / CSI measurements on high-band are crucial for meaningful DL throughput
  Aperiodic CSI-RS operation only realistic solution to provide channel measurements for high-band
  Triggering of the CSI-RS reports on the FR1 whenever needed seems to be increasingly important given RAN4 relaxations of maximum UL output power and large tolerances. The FR2 connection will not be DL-limited.
Uplink coverage in high-band is limited
  For Inter-band CA operation between low-band and high band, beam/CSI measurements on high-band should be reported via low band
Low band
HB (UL)
High band (HB)
Low band (LB)
DL
UL
HB (DL)
Inter-band CA deployment based on Rel-15 is significantly important for many operators
Beam/CSI report on low band enabled by inter-band CA can drastically improve coverage for mmWave deployments

## Slide 6: Importance of CSI-RS triggerring by a carrier w different SCS
UE backwards compatibility and release independence for CA band combinations
FR1 + FR2 band combinations in Rel-15:
the following band combinations are specified in Rel-15:
  FR1+FR2: CA_n8-n258, CA_n71-n257, CA_n77-n257, CA_n78-n257 and CA_n79-n257
    (i.e. 900 MHz + 26 GHz and 600 MHz/3.5 GHz + 28 GHz)
specified for the same configuration in the DL and UL (i.e. both DL and UL aggregation with one carrier per band)
UEs supporting UL aggregation shall support fallback band combinations*
FR1 inter-band CA band combinations in Rel-15:
FR1 inter-band CA combinations between refarming bands and new sub-6GHz bands, since 15kHz SCS probably will be used for refarming bands, and 30kHz SCS will be used for new sub-6GHz bands.
There are already several combinations defined in Rel.15 RAN4 specs, for example: CA_n3-n77, CA_n3-n78, CA_n3-n79, CA_n8-n75, CA n8-n78, CA_n8-n79, CA_n28_n7
Implications of not approving the RAN1 CR for Rel-15:
fallback to DL Sell in FR2 (release of the FR2 UL Scell in coverage-limited areas) impaired or does not work
UEs only supporting DL Scell operation in FR2 impaired or would not work
For CA band combinations specified in Rel-16 and later with the RAN1 CR approved for Rel-16:
fallback to DL Scell in FR2 can not be release indepenent back to Rel-15 (no RAN1 signaling support)
*)From 38.306: Fallback band combination: A band combination that would result from another band combination by releasing at least one SCell or uplink configuration of SCell.

## Slide 7: Proposals
Adopt the following proposals:
Proposal:
  Clarify that scheduling PUSCH on Carrier X carrying an aperiodic CSI report for Carrier Y with carriers X and Y having different numerologies is not considered cross-carrier scheduling
    This feature is not excluded from Rel-15
Proposal:
  Adopt the companion 38.214 CR (RP-190632) correcting aperiodic CSI-RS slot offset and aligning the procedure for determining CSI-RS resource for measurement with already existing behavior in Rel-15 (e.g. PDCCH and PUCCH with different numerologies)
    Whether UE supports aperiodic CSI-RS triggering with different numerology from PDCCH is indicated as new UE capability per band combination, adopt accompanying 38.331 and 38.306 CRs (RP-190633 and RP-190634)

## Slide 8: CR (RP-190632) to determine the CSI-RS Resource
Determination of the CSI-RS resource needs clarification on the reference slot from which the slot offset obtained from CSI-RS configuration is to be applied
The CR aligns the procedure for determining the reference slot with the already existing behaviour in Rel-15 (e.g. PDCCH and PUCCH with different numerologies)
  The reference slot on the carrier with CSI-RS resources is subsequent slot to the latest slot that overlaps with the slot containing DCI
  The slot offset is based on the numerology of the carrier with CSI-RS
UL
PUSCH
DCI
Self -scheduling PUSCH with A-CSI report
Carrier X (µ1)
Carrier Y (µ2)
µ1≠µ2
A-CSI report
CSI-RS resources for measurement obtained from configuration
CSI-RS
Reference Slot

## Slide 9: CR (RP-190632) w additioanl UE processing relaxations
In order to not require UE to buffer data for slots in a higher numerology in anticipation of potential aperiodic CSI-RS trigger from a lower numerology, the proposal limits possible CSI-RS triggering offsets to only occur in later slots than the last slot overlapping the PDCCH slot
To avoid too short time between DCI decoding and presence of triggered CSI-RS when the PDCCH SCS is smaller than the CSI-RS SCS (
  The UE does not expected a triggering DCI in the last 10 symbols of the slot
  Added symbols to the scheduling offset threshold of aperiodic CSI-RS where the UE should apply a default QCL assumption
Carrier Y (µ2)
DCI
Carrier X (µ1)
µ1<µ2
✔
✔
✔
✔
CSI-RS trigger offset

## Slide 10: Example of slot offset calculation based on CR (RP-190505)
Carrier X ()
Carrier Y ()