## Slide 1
Discussion on the applicability of DFT-S-OFDM for NTN
CAICT，BUPT，CATT
2019.9
RP-191748

## Slide 2
Discussion 1: Possible solution of OFDMA in NTN
Discussion 2: Performance of DFT-s-OFDM under Nonlinear HPA
Discussion 3: PAPR reduction methods
Key factors of OFDMA application in NTN

## Slide 3
The Simulation Parameters
Conclusion：
1.PAPR of DFT-S-OFDM is 2~3dB lower than that of OFDMA.
2.The value of PAPR increases as the number of subcarrier numbers increases.
Possible solution of OFDMA in NTN | OFDMA DFT-s-OFDM
Subcarrier numbers (Useful subcarrier numbers) | 1024(853),2048(1705),4096(3409),8192(6913)
Number of symbols | 14000
Encoding method | BCH+LDPC
Modulation method | 16QAM
Code rate | 1/2
DFT-s-OFDM
OFDMA
Discussion 1: Possible solution of OFDMA in NTN
Notes: （1）仿真参数补充完整
（2）初步结论补充。

## Slide 4
The Simulation Parameters
Conclusion：
1.In case of the same BER requirements(), nonlinearity of HPA causes 1dB deterioration of SNR.
2. As OBO increases, SNR degradation decreases.
Discussion 2: Performance of DFT-s-OFDM under Nonlinear HPA
Subcarrier numbers (Useful subcarrier numbers) | 2048(1024)
Encoding method | BCH+LDPC
Modulation method | QPSK
Code rate | 1/2
CP length | 205
OBO | 0,1,2,3,4,5(dB)
DFT-S-OFDM
Notes: （1）仿真参数补充完整
（2）初步结论补充。

## Slide 5
1.Clipping: When PAPR is reduced, it will bring additional signal nonlinear distortion and deteriorate the signal EVM.
2. GPO(Generalized Precoded OFDMA): GPO has a lower PAPR value, but the processing flow is more complicated.
Discussion 3: PAPR reduction methods
Reduction methods | 1.Clipping 2.GPO
Subcarrier numbers (Useful subcarrier numbers) | 2048(1024)
Encoding method | BCH+LDPC
Modulation method | QPSK
Code rate | 1/2
CP length | 205
The Simulation Parameters
Conclusion：
GPO
Clipping
Notes: （1）仿真参数补充完整
（2）初步结论补充。

## Slide 6
Summary
1: Both OFDMA and DFT-s-OFDM could be used in NTN;
2: PAPR of DFT-s-OFDM is 2~3dB lower than that of OFDMA;
3. PAPR can be reduced by GPO and clipping;
4. We have already started the TA and PDSCH design of DFT-s-OFDM,
It could be discuss on next meeting.

## Slide 7
Thank You！