## Slide 1
Motivation for new WID on NR support for medium-to-high speed train scenario for FR2 PCell
Nokia, Nokia Shanghai Bell, Verizon
RAN#88-e 29th June – 3rd July 2020
RP-200847

## Slide 2
Motivation for new WID on NR support for medium-to-high speed train scenario for FR2 PCell
FR2 high-speed train scenario is one deployment scenario in TR 38.913
Current HST scenario work has considered only:
  FR1
  max Doppler shift of 3334 Hz
Hence Rel-16 NR does not include UE RRM requirements, UE demodulation requirements or BS demodulation requirements for high speed train scenarios for FR2
  Performance of the high speed scenario with high frequency and high velocity cannot yet be guaranteed
FR2 offers wider bandwidths and higher capacity than FR1, but consistent passenger user experience cannot be assured

## Slide 3
Scenario
Motivation for new WID on NR support for medium-to-high speed train scenario for FR2 PCell
The earliest scenario for imminent deployment is identified as follows:
  High-power UE devices mounted on the train carriages
  NR SA with PCell in FR2
  Band n261 (28 GHz)
  Maximum train velocity of 250 km/h
This would give a typical Doppler shift of up to 13.3 kHz

## Slide 4
Objectives (see RP-200846 for more detail)
Motivation for new WID on NR support for medium-to-high speed train scenario for FR2 PCell
Identify the channel model:
  HST-SFN scenario, i.e. multiple RRHs connecting to one BBU
  HST single tap channel model open-space
    Other channel models are not precluded
Determine the maximum Doppler frequency to be supported:
  Target band n261
  Actual maximum supported velocity to be decided, considering speeds of up to a maximum of 250km/h
Specify the UE RRM core requirements for Connected mode:
  Cell identification requirements
  Measurement delay requirements
  Beam management related requirements, e.g. L1-RSRP measurement
  Impact on RLM and UL timing.
Specify RRM performance requirements of measurement accuracy.
Specify the RRM test cases related to the new core requirements
Specify the UE demodulation requirements and test cases for at least PDSCH
Specify the BS demodulation requirements and test cases for at least PUSCH