## Slide 1
PC2 EN-DC FDD+TDD HPUE
China Unicom
3GPP TSG RAN Meeting #88e RP-200996
Electronic Meeting, June 29- July 3, 2020

## Slide 2: Background
Original target on finishing this WI was in RAN#87, but discussions on open issues (quoted on following pages) didn’t go smoothly, no agreements could be made in RAN4 meetings in April and May. New target of WI completion is further extended to RAN#89 in September 2020.
The objective of this WI is to specify the standard needed for Power Class 2 (PC2) high power UE for EN-DC for 1 LTE FDD band and 1 NR TDD band (23dBm LTE + 23dBm NR and 23dBmLTE + 26dBm NR). The scope of this WI is the example band combination DC_3A_n78n. Specifically, it includes the following aspects:
Design the UE capability report signalling and facilitate SAR compliance based on the outcomes of the studies in TR 37.815
Standardize RF requirements
Evaluate any additional impact to the requirements due to the high power on UL.
Note: RAN4 needs to discuss whether existing RAN2 signalling can be reused to solve the issues in this WI. If there is RAN2 signalling impact then RAN4 will send LS to RAN2 to inform the solution. No RAN2 TUs are requested for this WI.

## Slide 3: Open Issue - 1
Issues on “blind” scheme (scheme of reducing LTE FDD power)
  Option 1: Not to include “blind” scheme at current stage. (Samsung, Xiaomi, Qualcomm, ZTE, CHTTL, Huawei, OPPO, CU, vivo)
  Option 2: Introduce the “blind” scheme as the baseline. (Ericsson, Vodafone, T-mobile)
  Option 3: Introduce a new item in UE signalling to indicate if “Reduce_FDD_power” is supported. ([vivo])
  Option 4: Introduce “blind” scheme as an option, and UE-based SAR management described in R4-2006654 as the default UE behavior baseline.
  The benefits and the impacts on UE side when introducing the “blind” scheme as the baseline had been further discussed in two meetings, but companies cannot reach consensus.

## Slide 4: Open Issue - 2
Choosing “default value” or “blind scheme” when capability parameters are absent
  Option 1: Using default value of maxNRDuty for two cases of LTE and NR power combination (Samsung, Xiaomi, Qualcomm, ZTE, [Huawei], CU, vivo)
  Option 2: Following “blind” scheme by reduced power (PLTE) and use of the common UL-DL patterns on the TDD CG (Ericsson, Vodafone, T-mobile)
  Option 3: Assume “Full duty support” when capability parameters are missing(Huawei, OPPO)
  Option 4: Assume “UE-based” SAR management when capability parameters are absent.

## Slide 5: Open Issue - 3
Choosing “PC fallback” or “blind scheme” when the UL EN-DC scheduling exceeds the UE capability
  Option 1: UE should fallback to PC3 (Samsung, Xiaomi, Qualcomm, ZTE, [CHTTL], Huawei, OPPO, CU, vivo)
  Option 2: “Blind” scheme should be followed (Ericsson, Vodafone, T-mobile)
  Option 3:UEs fallback to PC3 when UL EN-DC scheduling exceeds the UE capability, but add a conditional statement for 100% UL percentage with an upper limit of the UL power setting on the LTE side for each fixed LTE reference configuration. (CHTTL, [vivo])
  Option 4: UE-based scheme followed when the UL EN-DC scheduling exceeds the UE capability.

## Slide 6: Summary
Observations:
  Agreements on the above open issues could not be reached.
  As a consequence, operators who had urgent need to deploy FDD+TDD EN-DC PC2 UE for band combination DC_3A_n78 as a Rel-16 feature could not have commercial deployments until much later time.
Proposal:
  We propose to finalize the WI as soon as possible. If agreements or compromises on whether or not to include blind scheme could not be made. Then follow majority view to set the duty cycle based scheme as solution to keep align with SI conclusion, and further treat blind scheme at later stage.

## Slide 7: Reference
[1] R4-2005707 Email discussion summary for [94e Bis][26] ENDC_UE_PC2_FDD_TDD, Moderator (China Unicom)
[2] R4-2005188 WF on PC2 EN-DC FDD+TDD HPUE, China Unicom
[3] R4-2008959 Email discussion summary for [95e][131] ENDC_UE_PC2_FDD_TDD, Moderator (China Unicom)
[4] R4-2008907 WF on PC2 EN-DC FDD+TDD HPUE, China Unicom

## Slide 8
Thank you!